Apple //e Hardware Technical Note #8 - Known Anomalies of
 the New //e ROMs
 
 Written:                                       6/84
 Verified by: Cameron Birse                     2/86
 
 ------------------------------------------------------------
 
 This technical notes describes three current problems, and
 some possible workarounds for them.
 
 ------------------------------------------------------------
 
 The following three anomalies are known to occur when the
 new //e ROMs are present:
 
 1)  If the new //e ROMs are used with interrupts active when
 a combination of certain printer cards (Versacard, Uniprint,
 Graphitti, PSIO cards) along with the mousecard are present
 in the system, the system will hang when printing is
 attempted.  This is possibly caused by a spurious interrupt
 occurring from the mousecard.  The problem can be avoided by
 disabling interrupts while printing to a printer card.  For
 more information on the general architecture of the //e and
 how the ROMs handle them see: "Interrupts on the Apple //e"
 by Ernie Beernink, 20-May-84.
 
 2)  There may be some problems when using the ROMs with
 communications packages.  This is due to the way that the 80
 column firmware switches into 40 column mode.  By sending a
 control-Q through COUT the firmware to switches into 40
 column mode.   A simple solution to this would be to send an
 ESC-CTL-D sequence which disables the control functions.
 This will remain in effect until either the 80 column card
 is re-initialized by PR#3 or an ESC-CTL-E is sent through
 COUT.  Another solution would be to simply not allow
 control-Q's to get through to COUT by filtering them before
 they get there.
 
 3)  Many developers using double high resolution
 (dbl-hi-res) graphics may wish to use 40 column text
 displays so that the text can be read on a television set.
 There are a couple of possibilities:
 
 A.)  You can define your own dbl-hi-res character set with
 any size characters you desire and then plot them on the
 dbl-hi-res screen.
 
 B.)  You can print text to the Apple //e text screen and
 toggle the screen on to display it.
 
 NOTE: There is no way to display 4 lines of 40 column text
 at the bottom of the dbl-hi-res screen in mixed mode since
 the 80 column hardware must be active while dbl-hi-res is
 being displayed.
 
 #To use the second method, however, does require some
 special considerations.
 
 The Apple //e scroll routines continues to use the window
 parameters when scrolling, but uses the 80COL softswitch to
 determine if it should scroll the 80 or 40 column screen.
 Since the firmware has initialized a 40-column window, the
 scroll routines will move only the first 40 columns.  But,
 the 80COL flag has been turned on for dbl-hi-res!
 Therefore,
 the scrolling routine takes every even column from auxiliary
 memory and every odd column from main memory.  As a result,
 only the first 40 columns get scrolled, 20 columns from
 auxiliary memory and 20 columns from main memory.
 
 One possible solution to the problem is to write your own
 scroll routines.  Another might be to write to the screen so
 that scrolling will not occur.  But there is yet another
 solution.  Turn on the full 80 column mode with a "PR#3" or
 the equivalent.  Now print your text to COUT in the normal
 manner being careful not to exceed 40 characters per line.
 The 80 column firmware will scroll everything properly.
 When you are ready to display text, send a CONTROL-Q through
 COUT to switch to 40 columns.  When you are ready to return
 to dbl-hi-res mode, send a CONTROL-R to COUT.
 
 When switching modes, a momentary "glitch" may occur.  If
 you send the CONTROL-Q to COUT while still in graphics mode
 the screen will go to regular "single" hi-res mode before
 finally going to text mode.  If you switch to text mode
 first, the text will be in 80 column mode (with 40 columns
 displayed on the left half of the screen) before ultimately
 going to 40 column mode.  The same potential glitch may
 occur going back to dbl-hi-res.  The "glitch" will be only
 momentary and may not present any problem for your
 application.