File Attribute Zapper II
                        Version 2.3
           Public-Domain Software by Bruce A. Mah
                      January 29, 1989

Introduction
     This program allows you to easily change the primary 
type, auxiliary type, and access bits of any ProDOS file.  
It's useful if, say, you accidentally downloaded a binary file 
from a telecommunications service as a text file or some 
such thing as that.
     FAZ II differs from other "filetype changing" programs 
in that it allows you to also change the auxiliary types and 
access bits of files.

A Little Background
     For interested parties, here's the scoop on filetypes 
and access bits.  Each ProDOS file possesses a primary and 
auxiliary filetype.  They define "what" a file is; programs 
can identify their own files by assigning them unique 
combinations of primary and unique filetypes.
     Primary filetypes are one byte long and can have one of 
256 different values, from 0 to 255.  Auxiliary filetypes 
are two bytes long and can take on one of 65,536 different 
values.
     Originally, primary filetypes were intended to identify 
files and auxiliary filetypes were meant to provide 
additional information to programs using those files.  For 
example, AppleWorks Word Processor files have primary type 
$1A.  Their auxiliary types hold the status of each letter 
in the filename as upper or lower case.
     Over the years, it became apparent that ProDOS was 
going to "run out" of primary filetypes, as programmers used 
more and more primary types for their own uses.  Apple 
Developer Technical Support stepped in and defined some new 
"generic" primary filetypes.  The auxiliary type of these 
files indicate what program created the file.  For example, 
primary type $D5 defines a "Music Sequence" file and the 
combination of primary type $D5 and auxiliary type $8001 
indicates a file for "Diversi-Tune" by DSR, Inc.
     The file access bits define the ways in which a file 
may be accessed (make sense?).  These control whether or not 
a file can deleted, renamed, written to, or read, and also 
indicate whether or not the file has changed since its last 
backup and whether or not the file should be "invisible."

Required
     FAZ II requires an enhanced Apple //e, an Apple //c or 
//c Plus, or an Apple IIgs.  If you don't have either of 
these, get FAZ 1.2 (the previous version of this program).

Running FAZ II
     This is pretty simple...just launch the program FAZ.II 
from a program selector or AppleSoft Basic (in the latter 
case, type "-FAZ.II").
     After a title page, you'll be presented with FAZ II's 
main menu.
     Housekeeping stuff:  "Q" does a ProDOS Quit call and 
will return you to a program selector if you used one.
     "P" allows you to set a new ProDOS prefix.  If you try 
to do something fishy, FAZ II will, of course, yell at you.
     "C" to change a file's attributes is (hopefully) why 
you ran this program in the first place.  The next few 
sections describe what happens when you choose this command.

File Selection and Operations
     While selecting a file to work with, you can use the 
arrow keys and Return to select a file.  The display will 
scroll to show additional files.  You can enter 
subdirectories by selecting them, and "pop out" by selecting 
the "Parent directory" entry.  If you try to "pop out" of a 
volume's main directory, you'll be presented with a menu 
that allows you to switch volumes.  Finally, Escape returns 
you to the main menu.
     Note that if you want to work with files in a directory 
which is more than one or two subdirectories away from the 
current directory, it may be faster to return to the main 
menu and use the "P" command to set a new prefix rather than 
trying to traverse through the directory structure.  I think 
that sets some kind of record...the first part of this 
paragraph is all one sentence!
     Once you've chosen a file, you'll see some analysis of 
the primary and auxiliary filetypes, and a listing of the 
activated access bits.

[A] Change Access Bits
     Allows you to modify the kinds of ways in which ProDOS 
can access this file.  You can independently set any of the 
following bits:  Destroy (delete), Rename, Backup, 
Invisible, Write, and Read.  This command is useful if you 
want to set up non-standard permission on a file (i.e. you 
want to be able to rename and read, but not destroy or write 
a file).

[F] Change complete Filetype (automatic)
     This allows you to change the primary and auxiliary 
types of a file according to a pre-defined list of file 
types.  Simply scroll up and down to find the filetype you 
want to use, and press RETURN to select it.  Easy!

[P] Change Primary Type
     Change the primary filetype of this file; you'll be 
asked to enter the new type in hexadecimal.
     I made the program ask in hex for two reasons:  1) 
Hexadecimal is the most-used numbering system for filetypes 
on the Apple.  2) If you're using this command, it's 
somewhat assumed that you know what you're doing and won't 
be put off by a little bit of base-16 numbers.  3) It's a 
heck of a lot easier to write a hex conversion routine than 
a decimal conversion routine.

[X] Change Auxiliary Type
     This command asks you for a new auxiliary type for a 
file.  Again, enter the new type in hexadecimal (see "P" 
above for my reasoning).

ESC Return to file selection menu
     Wonder what this option does...

Customizing FAZ II
     Unlike FAZ I, FAZ II is _not_ user-customizeable.  For 
various reasons, mostly arising from the fact that FAZ is 
now written in assembly language, adding filetypes to FAZ II 
is a more complex process, impractical without the source 
code.
     On the other hand, I'm quite open to suggestions as to 
filetypes to add.  If you run across new ProDOS filetypes 
you think should be added to the program, please contact me 
at one of the electronic mail addresses listed below and 
I'll incorporate them into the next version.
     Back on the first hand, if you need to use some weird 
filetypes that no one else uses, you're probably better off 
sticking to FAZ I and its easy-to-change filetype list.

Other Notes
     This is a useful little program, but, like any utility 
program can cause havoc if used carelessly or improperly.  
Let's be careful out there...
     FAZ II is sort of a kludge.  It was thrown together out 
of parts of other programs (anyone here used my Three-Column 
Printer?) in the first three days of my winter vacation.  
Hopefully I did a good job of hiding this fact but then who 
am I deluding?  Just let me know when you find the bugs!
     Much of the filetype data in this program was taken 
from the following sources:  "File Type Changer" by Roger 
Wagner Publishing (a utility program included with Merlin 
8/16).  GS/OS Reference, Volume One, Beta Draft, from 
APDA.  Apple II Filetype Notes, by Apple Computer, Inc.
     Rick Oshlo, John Clary, and Tony Pizza provided some 
valuable assistance (read "bug reports") with FAZ I.  
Thanks, guys!

Feedback
     Feedback, comments, and gripes can be directed to me at 
the following e-mail addresses:

GEnie:  B.MAH
CI$:  72406,350
AppleLink PE:  BruceAMah

Revision History
Version 2.0--Original version of FAZ II.  This is a complete 
rewrite of FAZ, version 1.0, done completely in 65C02 
assembly language.  No additional capabilities added, but a 
considerable speed improvement over FAZ I.  Minor changes 
made to this documentation file to reflect changes in the 
program.

Version 2.1--Eric Mueller (A2Pro Leader on GEnie) pointed 
out the need for a command to enter the prefix for those 
tortured souls (like himself) who have seven or eight levels 
of subdirectories.  This has been added on the main menu.
     It is no longer possible to zap normal files to 
directory files using the automatic filetype change command 
If you really want to do it, you can still do it using the 
primary filetype change command.  But you shouldn't be doing 
that anyway.  Note that it has NEVER been possible to zap 
directories to normal filetypes.
     Filetypes for some more APW (Apple Programmer's 
Workshop) source files were added; existing types were 
cleaned up a bit.
     Source files were also cleaned up and restructured (not 
noticeable from the user level).

Version 2.2--Tim Swihart suggested support for the 
"invisible" bit for GS/OS.  This has been added...effect of 
this bit upon ProDOS 8 and ProDOS 16 is unknown.  It is 
believed that these operating systems and existing utilities 
will ignore this bit, but caveat user.
     This version wasn't released for general distribution, 
but there may be a few copies floating around out there.

Version 2.3--This version was released in response to Apple 
Computer's publication of its "File Type Notes" in January 
1989.  New filetypes from the FTNs were added and existing 
types were cleaned up considerably, but no changes were made 
to the actual program code.

----------

"Don't you just love personal software with little asides 
like this? I can do that because it's my company and there's 
no one to tell me that this is unprofessional. Who cares?"

--Randy Brandt, in the "Patchmania" file on the PathFinder 
  disk, published by JEM software.