APPLE II KERMIT USER GUIDE


                                 VERSION 3.87

                                Ted Medin, NOSC



                                  1990 Oct 10



                            Copyright (C) 1981,1989
            Trustees of Columbia University in the City of New York

     Permission is granted to any individual or institution to use, copy,
    or redistribute this document so long as it is not sold for profit, and
                  provided this copyright notice is retained.

1. Apple II Kermit                                                       Page 1

-------------------------------------------------------------------------------
1. Apple II Kermit

Authors:    Antonino N. J. Mione (Stevens Institute of Technology),
            Peter Trei (Columbia University),
            Ted Medin (NOSC),
            Bob Holley (SERDAC)

Version:    3.87

Date:       1990 Oct

Kermit-65 Capabilities At A Glance:

  Local operation:                   Yes
  Remote operation:                  Yes
  Transfers text files:              Yes
  Transfers binary files:            Yes
  Wildcard send:                     Yes
  ^X/^Y interruption(Q):             Yes
  Filename collision avoidance:      Yes
  Can time out:                      Yes
  8th-bit prefixing:                 Yes
  Repeat count prefixing:            No
  Alternate block checks:            No
  Terminal emulation:                Yes (VT52, VT100)
  Communication settings:            Yes
  Transmit BREAK:                    Yes
  IBM communication:                 Yes
  Transaction logging:               No
  Session logging (raw download):    Yes
  Raw upload:                        No
  Act as server:                     Yes
  Talk to server:                    Yes
  Advanced commands for servers:     Yes
  Long packets:                      Yes
  Sliding windows:                   No
  Local file management:             Yes
  Handle file attributes:            Yes
  Command/init files:                Yes
  Printer control:                   Yes

Kermit-65  is  a  program that implements the Kermit file transfer protocol for
the Motorola 6502 processor family (hence the name, Kermit-65) on the Apple  II
microcomputer  system.   It is written in 6502 assembly language and should run
on any Apple II or compatible running DOS 3.3 or PRODOS.    This  section  will
describe  the things you should know about the file system in order to make ef-
fective use of Kermit, and then it will describe the special  features  of  the
Kermit-65 program.

1.1. Supported Systems and Devices                                       Page 2

-------------------------------------------------------------------------------
1.1. Supported Systems and Devices

There  are  several  different Apple II's which can run Kermit-65.  Kermit will
have no problems running on an Apple II, II+, //e, //c or //gs system.  Of  the
different  communication devices available for the Apple II, Kermit-65 supports
the ones shown in Table 1-1.

-------------------------------------------------------------------------------



               AE Serial Pro (super serial driver - sw 1 & 3 open 2 & 4 closed)
               AIO II (Uses the Apple Com Card driver??? - untested)
               ALS dispatcher (Uses the Apple Com Card driver)
               Apple Cat Serial Card
               Apple Com Serial Card
               ASIO (Uses the Apple Com Card driver??? - untested)
               Apple Super Serial Card & //c Serial Port
               Apple //gs Serial Port
               CCS 7710 Serial Card
               CCS 7711 (Uses the Apple Com Card driver??? - untested)
               D.C. Hayes Micromodem.
               Microtek sv-622 Card
               Prometheus Versacard (Uses the Apple Com Card driver)
               SSM AIO (Uses the Apple Com Card driver??? - untested)

        Table 1-1:  Apple II Communication Cards Supported by Kermit-65

-------------------------------------------------------------------------------

It is possible that other  cards  may  have  operational  characteristics  very
similar  or  identical to one of the devices above. If this is the case, it may
work using one of the currently available device drivers.  The user may want to
try  each  of  the above options to see if any of them work.  Kermit-65 must be
told in which slot the card resides.  This may be done with the  'SET'  command
(documented below).


1.2. The DOS 3.3 File System

Items  of  importance which will be discussed in this section include filenames
and file characteristics.


    Apple DOS Filenames

Filenames under Apple DOS may contain almost  any  ASCII  character  (including
space). It is not recommended that special characters, (i.e. control characters
or spaces) be used in a filename to be transferred by Kermit-65 since they  may
cause problems when parsing the filename.  Filenames may be up to 40 characters
in length.


    Apple DOS File Characteristics

All files in Apple DOS have a file type associated with them which is contained

1.2. The DOS 3.3 File System                                             Page 3

-------------------------------------------------------------------------------
in  the  directory  entry  for the file but is not part of the filename itself.
There are four types of files in DOS 3.3. They are:

   1. APPLESOFT BASIC
   2. INTEGER BASIC
   3. BINARY
   4. TEXT

All file types have their data stored in eight-bit bytes although  not  all  of
them need the eighth bit. The two file types containing basic programs required
the eighth bit due to the nature of the data being  stored.  BINARY  files  are
images  of  memory  copied into a file. Often, these are machine code programs.
These files require all eight bits. TEXT files normally contain only  printable
or  carriage control characters. They are stored in the form of seven-bit ASCII
characters but the eighth bit should always be set since Apples manipulate  all
text internally as 'Negative ASCII'.  When transmitting non-text files the user
must insure that both Kermits are handling eight-bit data  so  that  no  infor-
mation  is  lost.  If  an eight-bit data path is not available (i.e. the remote
Kermit needs to do parity checking with the eighth bit), then eight-bit quoting
should  be used.  Of course, BINARY files as well as Apple BASIC files will not
have much meaning on a different system.  If the user desires to edit  a  BASIC
file  on  a mainframe, for instance, s/he must convert it to a TEXT file before
sending it over. After receiving the file back on the Apple, the user may  con-
vert  it back to BASIC once again.  The reason BASIC files would be meaningless
to a different machine is that  the  Apple  stores  BASIC  keywords  as  single
character tokens to save space and processing time.  To convert a BASIC program
to and from a TEXT file, consult the Apple DOS 3.3 Manual.    File  information
can be obtained by issuing the CATALOG command.  For example:

    ]CATALOG

     DISK VOLUME 010

       *A 002 HELLO
        B 078 KERMIT
        A 002 READER
        T 005 TESTFILE

    ]

When  Kermit-65 is receiving a file, the file it creates on diskette will be of
the type indicated by the FILE-TYPE parameter.  The file will always be left in
an  unlocked  state  after  it  is  closed  by Kermit-65.  When sending a file,
Kermit-65 will use the FILE-TYPE  parameter  to  determine  how  to  detect  an
End-of-file  condition.  Thus, it is important to have this set properly in all
cases.


    Recommendations for Archiving Files

When using a large system for archiving purposes, there is no reason to convert
Apple Basic programs into text files before sending them if there is no need to
edit them on the mainframe.  The FILE-TYPE parameter must always  be  set  cor-
rectly when sending and receiving files.  The procedure for archiving files is:

   1. Run Kermit on remote system.

1.2. The DOS 3.3 File System                                             Page 4

-------------------------------------------------------------------------------
   2. SET FILE-TYPE TEXT (or APPLESOFT or ...) on Kermit-65.

   3. Send the files.


1.3. The PRODOS File System

The  PRODOS system is essentially the same as the DOS system with the exception
that performance has been improved, hardware usage has been expanded  and  file
names have different syntax.  File names are the major importance to the Kermit
system.  File names have the following syntax:

  /volname/subdirectory1/.../subdirectoryn/filename

where "volname" is the volume name where the file is located.   Subdirectory(n)
is  a  subdirectory  on the volume and may be omitted.  Filenames are much more
restrictive than DOS filenames.  PRODOS filenames are limited to 15  characters
with  no embedded spaces and few special characters, and must begin with an al-
phabetic character.  /volname/sub ...  may be omitted from the filename by  use
of the SET PREFIX command.

Binary  file  transfer  using  PRODOS  has its dangers when creating new files.
PRODOS keeps the file's size and starting location in the directory which is of
course  not  transferred.    Therefore a new binary file will have its starting
location 0 which can cause some interesting problems if you try  and  BRUN  the
file.  Basic files all start at $801 (it says here) so Kermit creates new basic
files with a starting address of $801.


1.4. Program Operation

Prior to using Kermit-65 for transferring files, the modem  interface  must  be
set  to  handle  data  in a certain manner.  First, the data format should be 8
data bits and 1 stop bit.  Second, the card should be set to no  parity.    The
baud  rate  (if  adjustable) must be set to whatever rate the modem can handle.
For the D.C. Hayes Micromodem, these parameters are set correctly  by  default,
so  very  little has to be done.  For the Apple Super Serial Card these are set
from within Kermit-65 except the interrupt switch (sw6-2) which must be set for
interrupts  on.   For the Microtek SV-622, all applicable parameters are set by
Kermit-65.  Some mainframes may need parity checking (i.e. most IBM  machines).
In  this  case  some  parity setting (other than none) will usually work.  When
talking with such mainframes, binary and basic files on  the  Apple  cannot  be
transferred  unless  Eighth-bit-quoting is acceptable to the host.  If you have
the parameters set correctly then the "CONNECT" command will start Kermit talk-
ing out the communication port.

File  transfer  is  very  dependent  upon  parity. Make sure the host and local
parity are the same. Following are a couple of site's method for file transfer.

We have an IBM 3033 and 4381 and use both 3705/3725 and 7171 or Series/1  front
ends.  The differences in front ends as far as any microcomputer Kermit is con-
cerned duplex (local-echo on for the 3705,  local-echo  off  for  the  7171  or
Series/1), parity (the two front ends might use different parity, e.g. Mark for
the 3705 and Even for the 7171), and flow control (None for the 3705,  XON/XOFF
for the 7171).

In Kermit-65, IBM mainframe users need to set the following parameters:

1.4. Program Operation                                                   Page 5

-------------------------------------------------------------------------------
    BAUD            Whatever is supported.

    PARITY          EVEN, ODD, or MARK, whatever your front end requires.

    FLOW            XON for the 7171, NONE for the 3705.

    FLOW DELAY      00

    LOCAL-ECHO      OFF for 7171, ON for 3705

In Kermit-65, SERDAC VAX 8800 users need to set the following parameters:

    BAUD            SERDAC Dial-up & 300, 1200, or 2400 baud
                    FIRN Dialup:(the highest your modem and the dial-up connec-
                    tion will support) )
                    Ethernet Hardwire: 300, 1200, 2400, or 4800 baud.

    PARITY          NONE

    FLOW            XON

    FLOW DELAY      00 (higher for printers, logging, or "slow" Apples)

    LOCAL-ECHO      OFF

    NOTE: If you want to do a binary  file  transfer  (Apple  binary  or  BASIC
                    files)  via  a  FIRN  Network  connection to the SERDAC VAX
                    8800, you must SET PARITY SPACE before the transfer is  in-
                    itiated;  that  will insure that eight-bit quoting is used.
                    If you dial directly into the VAX 8800,  SET  PARITY  NONE;
                    eight-bit  quoting  (which  is  less  efficient) is not re-
                    quired.


    Conversing With Kermit-65

Kermit-65 reads file KERMIT.INIT from the default  drive  when  started.    The
lines  of this file are executed one at a time starting at the beginning.  This
file should be an ASCII text file and  contain  commands  to  set  up  Kermit's
parameters as desired.  It will also execute Kermit's other commands.  However,
any command which reads a file (like MODEM) or leaves local mode (like CONNECT)
will  terminate  reading  of this file and continue with the command specified.
Use your favorite editor to produce this file.  Here's a sample:

  set display 80 3
  set keyboard 2e
  set baud 4800
  modem

Kermit-65's prompt is "Kermit-65>".  To run Kermit-65 and issue commands to it,
type "brun kermit".  Example:

  ]BRUN KERMIT

  NOSC/STEVENS/CU - APPLE ][ KERMIT-65 - VER 3.87

  Kermit-65>send testfile

1.4. Program Operation                                                   Page 6

-------------------------------------------------------------------------------
      (file is sent...)

  Kermit-65>status

      (performance statistics are printed...)

  Kermit-65>(other commands...)
            .
            .
            .
  Kermit-65>exit
  ]

Like  many  Kermit  programs,  Kermit-65  uses  a  DEC-20 style command parser.
During interactive operation, you may use the ?-prompting  help  feature  ("?")
and recognition (ESC) features while typing commands.  A question mark typed at
any point in a command displays the options available at that point; typing  an
ESC  character  causes the current keyword to be completed (or default value to
be supplied).  If you have not typed sufficient characters to uniquely  specify
the  keyword  (or if there is no default value) then a beep will be sounded and
you may continue typing.  Keywords may be abbreviated to  any  prefix  that  is
unique.


    Remote and Local Operation

Kermit-65  is  normally  run in local mode. It may be run as a remote Kermit as
well although there is no advantage to doing things that  way.  Kermit-65  sup-
ports User-mode commands for talking to a Server, and it does support a limited
server mode.


1.5. Kermit-65 Commands


1.5.1. The CATALOG Command

Syntax: CATALOG
    or LS

Typing CATALOG produces a catalog (directory) listing of your default drive.


1.5.2. The CONNECT Command

Syntax:  CONNECT

Establish a terminal connection to the remote system using all the current  SET
parameters  for  terminal  type,  speed, parity, etc.  Get back to Kermit-65 by
typing the escape character followed by the letter C. The escape  character  is
Control-@   by   default.     When  you  type  the  escape  character,  several
single-character commands are possible.  These are shown in Table 1-2.

You can use the SET ESCAPE command to  define  a  different  escape  character.
When CONNECTed, Kermit-65 will be passing characters entered on the keyboard to
the remote system, and passing characters from the remote system to  the  Apple

1.5.2. The CONNECT Command                                               Page 7

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



    ?     List all the possible single-character arguments.
    B     send a Break signal.
    C     Command mode (returning to kermit-65).
    D     Drop the phone line to the remote and return to Kermit-65.
    E     Erase the screen (useful for clearing garbage on screen).
    K     toggle Keypad application-mode on/off.
    M     execute the Modem command.
    P     toggle the Printer on/off.
    Q     execute the Quit command.
    R     pRint the screen, >= //e required
    S     show Status of the connection.
    V     cursor-keys-Vt100 toggle.
    W     sWap the del and backspace key.
    0     send a null (ASCII 0).
    ^@    (or whatever the Connect-Escape character is): send the
          Connect-Escape character itself.

        Table 1-2:  Kermit-65 Single-Character CONNECT Escape Commands

-------------------------------------------------------------------------------

screen.    Incoming  characters are interpreted according the selected terminal
type (see SET TERMINAL).

On an Apple II+ with an incomplete keyboard, special characters can be typed by
prefixing  regular  characters  with a right-arrow.  On uppercase-only screens,
uppercase characters are shown in inverse and  lowercase  characters  are  dis-
played as normal uppercase characters.

Here are the rules for using the special 2/2+ input, to get all printable ASCII
characters, and how they appear on the screen.  Special meanings are applied in
various  contexts to certain characters.  The left and right arrow keys do spe-
cial things, and sometimes the escape key does  as  well.    For  letters,  the
keyboard  is always in either default UPPERCASE mode or default lowercase mode.
When in UPPERCASE, all letters typed are sent out as uppercase.  In  lowercase,
all  letters  are sent as lowercase. To reverse the case for the next character
only, hit the right-arrow ("prefix") key.  To switch the default case, hit  the
prefix-key  twice  in a row.  For funny characters, the prefix key is also used
to get the unusual punctuation characters which are not on the Apple  keyboard.
Table  1-3  shows  the Apple II/II+ keyboard escapes; the letter "p" represents
the prefix character.

The left-arrow key sends a rubout (ASCII 127).  With left-arrow and right arrow
doing  special  things, it's a little hard to enter their characters (^H and ^U
respectively).  There is therefore an escape from prefix mode sequence.  If you
type prefix-ESC, the next character is sent without any interpretation.  If you
have the capability for upper/lower case, etc, then use the 'SET KEYBOARD'  and
'SET DISPLAY' commands to specify complete keyboards.

While  in  connect mode if you have a //e or better with 80 column display, the
cursor will blink. The rate of blink is tied  to  the  "SET  TIMING"  constant.
Also the screen will be restored to state of the previous connect(if any).

1.5.3. The DELETE Command                                                Page 8

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



    To Get                        Type      Appearance
    Left Square Bracket            p(          [
    Right Square Bracket           p)          ]
    Left Curly Bracket             p<          {
    Right Curly Bracket            p>          }
    Underline                      p-          _
    Backslash                      p/          \
    Tilde (wiggle)                 p^          ~
    Vertical Line                  p.          |

                   Table 1-3:  Apple II/II+ Keyboard Escapes

-------------------------------------------------------------------------------


1.5.3. The DELETE Command

Syntax: DELETE filespec
    or RM filespec

Typing DELETE causes the file specified to be deleted.


1.5.4. The EXIT and QUIT Commands

Syntax: EXIT or QUIT

Exit  from  Kermit-65. When using dos 3.3 you can probably restart the program,
provided you haven't run anything else, by typing 'CALL 4096'.


1.5.5. The GET Command

Syntax: GET remote-filespec[,local-filespec]

The GET command requests a remote Kermit server to send the file or file  group
specified by remote-filespec.  This command can be used with a Kermit server on
the other end.  The remote filespec is any string that  can  be  a  legal  file
specification for the remote system; it is not parsed or validated locally.  So
if  the  remote  Kermit  supports  wildcards  you  can  specify  them  in   the
remote-filespec.    Local-filespec  is optional and is the file name to be used
locally.  The "\" escape character may be used to accept the next character  of
the filespec asis and two escape characters will parse to a single "\".  If the
remote Kermit is not capable of server functions, then you will probably get an
error  message back from it like "Illegal packet type".  In this case, you must
connect to the other Kermit, give a SEND  command,  escape  back,  and  give  a
RECEIVE  command.   Currently, a packet can be retransmitted manually by typing
anything on the keyboard. If a 'Q' is typed, the entire  transmission  will  be
canceled.    During file transfer if the remote kermit supports file attributes
then the percent of the file transferred will be accurate else 0.

1.5.6. The HELP Command                                                  Page 9

-------------------------------------------------------------------------------
1.5.6. The HELP Command

Syntax: HELP

Typing HELP alone prints a brief summary of the Kermit-65 commands.


1.5.7. The LOCK Command

Syntax: LOCK filespec

LOCK will file lock the given filespec on the default drive.


1.5.8. The LOG Command

Syntax: LOG filespec

When connected to a remote  site,  log  the  remote  session's  output  to  the
specified  file.    The file type and file warning protocols are observed. This
command is dependent upon the flow control (XON/XOFF) working.    Without  flow
control  there  is little possibility of getting a correct copy of the terminal
session.  The logging begins when you connect to the remote and  is  terminated
when  you escape back to the local Kermit with the ESCAPE character followed by
the "C" command.


1.5.9. The MODEM Command

Syntax: MODEM

This command is designed for the hayes smart modem.  Typing  MODEM  causes  the
file  KERMIT.MODEM in the default drive/path to be used as a menu.  You will be
able to select any line in the file to be sent to the modem.  Sorry, you  can't
back  up  to  a previous menu, you will have to Quit and execute MODEM again. A
"CONNECT" response from the smart modem will cause Kermit to  leave  the  modem
command  and execute the CONNECT command. The Hayes smart modem must reply with
text status responses (not numbers).  One command per line  with  comments  al-
lowed  after  the first space (blank). Use your favorite editor to produce this
ASCII text file.  Since the attention Hayes command (AT) requires a  delay  the
"&"  character  becomes  the time delay for Kermit.  Each "&" causes a delay of
one second on a 6502 chip.  If you have a //gs or an accelerator board you  may
have  to  use  the  SET  TIMING  command to produce a one second delay.  If you
really need to send the "&" character to the modem then the "\" is  the  escape
character.  Put  a  "\" before any character and that character will be sent as
is. Of course two "\"'s will produce one "\".  Normally Kermit will wait for 27
seconds  (again  on  a  6502  chip) for the modem to respond, but any character
typed on the keyboard will terminate this wait. You may hear  the  busy  signal
and there is no sense waiting any longer, so hit (ouch!-not so hard) any key on
the keyboard.

Following is an example of the KERMIT.MODEM file:

  +++&&ATH    Get the Hayes Smartmodem's attention and then hang up.
  ATDP1234567 Call your local BBS with pulse dialing.
  ATDT8901234 Call your work dialup phone with touch tone dialing.

1.5.10. The RECEIVE Command                                             Page 10

-------------------------------------------------------------------------------
1.5.10. The RECEIVE Command

Syntax: RECEIVE [filespec]

The RECEIVE command tells Kermit-65 to receive a file or file  group  from  the
other system.  If only one file is being received, you may include the optional
filespec as the name to store the incoming file under; otherwise, the  name  is
taken  from the incoming file header.  If the name in the header is not a legal
filename, Kermit-65 will attempt  to  change  it  into  something  legal.    If
FILE-WARNING  is on and an incoming file has a name identical to a file already
existing on the diskette, Kermit-65 will issue a warning to the  user  and  at-
tempt  to  modify  the  filename to make it unique.  Currently, a packet can be
retransmitted manually by typing anything on the keyboard.  If a 'Q' is  typed,
the  entire  transmission  will be aborted.  During file transfer if the remote
kermit supports file attributes then the percent of the file  transferred  will
be accurate else 0.  Filespec is required when xmodem protocol is used.


1.5.11. The REMOTE Command

Syntax: REMOTE [option character-string]

The  only  option  currently  is  "kermit".  This  command  submits the command
"character-string" to the remote Kermit's command processor.  Long replies  are
not  paged so you will have to use ^S to stop the screen.  The obvious usage is
for setting and showing parameters on the remote Kermit.


1.5.12. The RENAME Command

Syntax: RENAME filespec,new-filespec

RENAME will rename filespec to new-filespec on the default drive.


1.5.13. The SEND Command

Syntax: SEND filespec[,remote-filespec]

The SEND command causes a file to be sent from the Apple to the remote  system.
The  Filespec  is  the  name of the file on the Apple diskette to be sent.  The
parser will not accept control characters and certain special characters  in  a
filename (like comma).  The "\" escape character may be used to accept the next
character of the filespec asis and two escape characters will parse to a single
"\".    Remote-filespec  is  optional and is the name of the file on the remote
kermit.  Thanks to Dick Atlee, wildcards are now acceptable when sending  files
(they  have always been acceptable when receiving files). The "*" is a multiple
character wildcard and the "=" is a single character wildcard.

The default disk drive is used for file transfers this can be changed with  the
'SET  DEFAULT-DISK'(DOS) or 'SET PREFIX'(PRODOS) command (explained below).  As
a file is being sent, the screen  displays  'RECEIVING  NUMBER  OF  BYTES'  and
'SENDING  NUMBER  OF  BYTES' with the decimal number of bytes transferred since
start of transmission.  If a packet must be transmitted several  times  and  it
reaches  the  maximum  retry count, the transfer will fail and the 'Kermit-65>'
prompt will return. If the remote Kermit sends an error packet, the text of the

1.5.13. The SEND Command                                                Page 11

-------------------------------------------------------------------------------
packet  will be displayed on the screen, the transfer will fail, and the prompt
will return.  Currently, a packet can be retransmitted manually by typing  any-
thing  on  the  keyboard.  If  a  'Q' is typed, the entire transmission will be
aborted.


1.5.14. The SERVER Command

Syntax: SERVER

Typing SERVER alone turns Kermit into a file server to a remote Kermit.    Cur-
rently  server  mode  will handle remote "send", "get", "remote" and "fin" com-
mands.  Variants of the above commands will probably work but file  serving  is
very  limited  at  present.  Because the Apple requires knowledge of file types
you can use the "remote Kermit" (or whatever the  remote  Kermit's  syntax  is)
command  to  set the file-type on the server.  Yes, the server will execute any
command so you can really get the server into trouble (this is not a BBS).  You
must  have  the  appropriate  file type set before transferring files.  You can
exit server mode by typing Control-C (^C) when not doing file transfers or  the
remote can of course terminate via the "fin" command.


1.5.15. The SET Command

Syntax: SET parameter [option [value]]

Establish  or  modify  various parameters for file transfer or terminal connec-
tion.  You can examine their values with  the  SHOW  command.    The  following
parameters may be SET:


    APPLICATION-MODE   Set VT100 gs keypad in/out of application mode.
                BAUD   Which baud rate should the com card use?
        CLEAR-SCREEN   Should screen be cleared when returning from connect?
   CURSOR-KEYS-VT100   In VT100 mode cursor keys give VT100 sequences.
           DEBUGGING   TERSE or VERBOSE packet information.
        DEFAULT-DISK   Which Diskette drive is used for DOS 3.3 file transfer?
             DISPLAY   Which type of screen display is being used?
              ESCAPE   Character for terminal connection.
           FILE-TYPE   Type of Apple file being sent/received.
        FILE-WARNING   Warn users if incoming file exists?
                FLOW   Should xon/xoff flow control be used to the remote?
            KEYBOARD   II+ or //e keyboard.
          LOCAL-ECHO   Full or half duplex switch.
              PARITY   Character parity to use
              PREFIX   Which default prefix to use with PRODOS?
             PRINTER   Should the printer be used for the display?
            PROTOCOL   Which protocol is to be used for file transfer.
             RECEIVE   Various parameters for receiving files
                SEND   Various parameters for sending files
                SLOT   Which slot # is communication device in?
                SWAP   Swap the del and backspace key?
               TIMER   Should Kermit observe the receive timeout value?
              TIMING   Change the time loop for 1 ms. delays.
            TERMINAL   Which type of terminal should Kermit emulate?

1.5.15. The SET Command                                                 Page 12

-------------------------------------------------------------------------------
    SET APPLICATION-MODE

Syntax: SET APPLICATION-MODE {ON, OFF}

For  VT100  emulation  with a gs keypad you can set the keypad in or out of ap-
plication mode. Some computer systems set this via escape sequences so  it  may
not be necessary to use this command.


    SET BAUD

Syntax: SET BAUD value

Value  is  the baud rate for your communication card.  For the super serial and
the microtek it can be 300 to 19200.  The actual values will  depend  upon  the
com card you are running with.


    SET CLEAR-SCREEN

Syntax: SET CLEAR-SCREEN {ON, OFF}

When  returning  from a connect the screen will be cleared if on. This is for a
//e or better machine.


    SET CURSOR-KEYS-VT100

Syntax: SET CURSOR-KEYS-VT100 {ON, OFF}

In VT100 emulation the cursor keys can also emulate the VT100 cursor keys.


    SET DEBUGGING

Syntax: SET DEBUGGING {TERSE, VERBOSE, OFF}

Record the packet traffic on your terminal.  Options are:  TERSE,  Show  packet
info only (brief).  VERBOSE displays packet field descriptions with packet info
(lengthy).   OFF  disables  display  of  debugging  information  (this  is  the
default).


    SET DEFAULT-DISK

Syntax: SET DEFAULT-DISK {SLOT, VOLUME, DRIVE} value

This  DOS  command will tell Kermit-65 which disk drive should be used for file
transfers.  The three parameters which may be set separately are  SLOT,  VOLUME
and  DRIVE.   The value for SLOT ranges from 1 to 7. The value for DRIVE is ei-
ther 1 or 2.  The value for VOLUME ranges from 0 to 255.


    SET DISPLAY

Syntax: SET DISPLAY {2E, 2P}

1.5.15. The SET Command                                                 Page 13

-------------------------------------------------------------------------------
    or SET DISPLAY 80-COL number

This command will tell Kermit-65 which kind of screen display you want to  use.
If you have an Apple II or II+ without an 80 column card, use the first syntax.
If you have any kind of an Apple with an 80 column card, enter: SET DISPLAY 80,
followed  by  a  space and the slot number where the card resides (if you don't
know the slot number, or the card is built-in to the set, try 3 ).


    SET ESCAPE

Syntax: SET ESCAPE hexadecimal-number

Specify the control character you want to use to "escape" from  remote  connec-
tions  back to Kermit-65.  The default is 0 (Control-@).  The number is the hex
value of the ASCII control character, 1 to 37, for instance 2 is  Control-B,  B
is Control-K.


    SET FILE-TYPE

Syntax: SET FILE-TYPE {APPLESOFT, INTEGER, TEXT, BINARY, OTHER hex-value}

This  will  inform Kermit-65 what type of file is being sent or received. It is
important that this is set correctly since Kermit-65 must create a file of  the
appropriate  type  when  receiving.  With the advent of file attributes (if the
other kermit does them) this has been improved  somewhat  but  since  file  at-
tributes  usually only knows about text and binary one may endup with the wrong
type.  So keep your type changing utility handy.  When Kermit-65 is sending, it
will  know  the  type of file but again be careful of file attributes (assuming
the other kermit does them) for the file may end up as binary on the other end.
The  keywords  for  this  parameter  are listed below.  OTHER includes an added
hex-value so that the user may specify the hex value of the  file-type.    This
has  meaning only in PRODOS and allows the user to specify any of the many dif-
ferent file types used in PRODOS, see Tables 1-5 and 1-6 (thanks to Phil Chien,
M L Stier et al).

    APPLESOFT       The file being transferred is an Applesoft Basic program.

    INTEGER         The file being sent/received is an Integer Basic program.

    TEXT            The file being sent/received is an ASCII Text file.

    BINARY          The file being sent/received is a Binary image.

    OTHER           The  type  of  file being sent/received is specified by the
                    hex-value.


    SET FILE-WARNING

Syntax: SET FILE-WARNING {ON, OFF}

This tells Kermit-65 whether to warn the user  about  incoming  filenames  con-
flicting with existing files or not.  If there is a conflict Kermit-65 will at-
tempt to change the file name to something unique.

1.5.15. The SET Command                                                 Page 14

-------------------------------------------------------------------------------
    SET FLOW

Syntax: SET FLOW {OFF, XON, DELAY number}

SET FLOW allows one to use the XON/XOFF protocol when  connected  to  a  remote
site.  Delay timings are part of this command.  Using delay times is probably a
desperation move to keep the screen/printer from losing  characters.    Setting
the timings will have to be set by experience.  Perhaps the best way to set the
timings is to bring the values down until you get failures and then double  the
timing figure.  Both LOG and SET PRINTER will probably depend on flow control.

    OFF             Turn off flow control

    XON             Turn on xon/xoff flow control with the remote

    DELAY number    Delay the micro until XOFF takes effect

Delay  followed by a number (including 0) delays the program for that many mil-
liseconds after the XOFF is given to the remote.  This delay allows the XOFF to
take effect before the program continues.

NOTE:  Except for printing and logging, most Apples will not require you to use
a flow delay, even at rates up thru 19200  baud;  for  proper  screen  control,
however,  certain  older  Apple  IIe's may require a fairly high delay (120-160
dec), even at 300 baud.


    SET KEYBOARD

Syntax: SET KEYBOARD {2P, 2E}

SET KEYBOARD tells Kermit-65 if the user has a full keyboard (2E) or not  (2P).
If  the  user  is  on  an  Apple  II+,  this  should be set to 2P (which is the
default).  When set to that, character translations are available by using  the
right-arrow key as a prefix character, as shown in Table 1-3.


    SET LOCAL-ECHO

Syntax: SET LOCAL-ECHO {ON,OFF} [Default: OFF]

This  command  tells Kermit-65 to echo to the screen characters you type on the
keyboard (LOCAL-ECHO = ON), or to let the remote system echo the typed  charac-
ters (LOCAL-ECHO = OFF).  If, when CONNECTed to the remote, you see a duplicate
of every character you type, escape back to Kermit-65, and SET LOCAL-ECHO  OFF.
If,  when CONNECTed to the remote, you see nothing echoed to the screen, escape
back to Kermit-65, and SET LOCAL-ECHO ON.


    SET PARITY

Syntax: SET PARITY {NONE, EVEN, ODD, MARK, SPACE} [Default: NONE]

This command tells Kermit-65 which parity you want to use  while  communicating
with the remote.  Most remotes use NONE; some use EVEN, a few may use the other
possible values. If you have a choice of parity to use with a  remote  machine,

1.5.15. The SET Command                                                 Page 15

-------------------------------------------------------------------------------
if possible, choose NONE.


    SET PREFIX

Syntax: SET PREFIX string [Default: boot volume]
    or CD string

This command allows you to specify a ProDOS volume/file prefix.


    SET PRINTER

Syntax: SET PRINTER {ON, SLOT} number
    or SET PRINTER OFF

This  allows  one  to turn the printer on for printing what is displayed on the
screen.  The printer can also be toggled on/off via the ESCAPE  character  fol-
lowed by the command "P".

Remember  when you use your printer there are a lot of variables here. What was
being sent to the screen now is being sent  to  your  printer.    If  you  were
emulating  the  VT52  your  printer  may  not know how to handle the escape se-
quences, tabs, etc. It may be you can tell the host you are a tty or some  such
device  that  will  produce  control  codes that your printer can handle.  Some
printers may require the flow control and delay to get readable printing.

    ON              Turn the printer on, slot number is required.

    OFF             Turn the printer off.

    SLOT number     Printer card is in slot "number".


    SET PROTOCOL

Syntax: SET PROTOCOL {KERMIT, XMODEM}

SET PROTOCOL tells kermit-65 which protocol to use for file  transfer.    NOTE:
When  XMODEM  is  used you will probably want to change the carriage return and
carriage return/line feed translation in the send/receive parameters.  eg. "SET
SEND CR<->CR,LF OFF" and "SET RECEIVE CR<->CR,LF OFF".


    SET RECEIVE

Syntax:  SET  RECEIVE  {CR-CR,LR,  EIGHT-BIT-QUOTE, END-OF-LINE, PACKET-LENGTH,
PAD-CHAR, PADDING, QUOTE-CHAR, START-OF-PACKET, TIMEOUT}

This will inform Kermit what to use to form and handle receive packets for file
transfer.

    CR<->CR,LF      {ON, OFF}
                    Terminate lines with cr or cr and lf.

    EIGHT-BIT-QUOTE hexadecimal-number

1.5.15. The SET Command                                                 Page 16

-------------------------------------------------------------------------------
                    Char for eighth bit quoting.

    END-OF-LINE     hexadecimal-number
                    Char for line termination.

    PACKET-LENGTH   hexadecimal-number
                    Size of packet.

    PAD-CHAR        hexadecimal-number
                    Char for padding.

    PADDING         hexadecimal-number
                    Number of padding chs.

    QUOTE-CHAR      hexadecimal-number
                    Char for quoting.

    START-OF-PACKET hexadecimal-number
                    Char for start of packet.

    TIMEOUT         hexadecimal-number
                    Number of seconds for timeout.


    SET SEND

Syntax:  SET  SEND  {CR-CR,LR,  EIGHT-BIT-QUOTE,  END-OF-LINE,   PACKET-LENGTH,
PAD-CHAR, PADDING, QUOTE-CHAR, START-OF-PACKET, TIMEOUT}

This  will  inform  Kermit what to use to form and handle send packets for file
transfer. The options are the same as the "SET RECEIVE ..." packets.


    SET SLOT

Syntax: SET SLOT number

This option tells Kermit-65 in which slot the communication device is  located.
The range for the number parameter is 1-7.


    SET SWAP

Syntax: SET SWAP {ON, OFF}

This  option  tells  Kermit-65  to  swap the functions of the del and backspace
keys.


    SET TIMER

Syntax: SET TIMER {ON, OFF}

SET TIMER will turn on or off the timeout checking for receive file  transfers.
Since there is no clock for exact timing a loop of instructions has been set up
assuming a 1 megacycle CPU.  CPUs which run faster may have to make  allowances

1.5.15. The SET Command                                                 Page 17

-------------------------------------------------------------------------------
via the SET RECEIVE TIMEOUT command or the SET TIMING command.


    SET TIMING

Syntax: SET TIMING { number }

Kermit uses a timing loop with the rom address $fca8 to produce a 1 ms.  delay.
If you have a machine that runs faster than the 6502 chip you may have  to  in-
crease this number to get the 1 ms delay.


    SET TERMINAL

Syntax: SET TERMINAL {MONITOR, NONE, VT100, VT52}

When  TERMINAL  is NONE, then all incoming characters (except nulls) are passed
directly to the display.

MONITOR emulation simply displays all the characters received from  the  remote
(except  nulls)  without  any formatting of the screen (40 or 80 characters per
line).  Control characters are displayed inverse.


VT100 Emulation

The Kermit-65 VT100 emulator is a small but working set of a  true  VT100  ter-
minal.    It  appears to work with most of the standard full screen editors and
processors on BSD UNIX and VAX/VMS machines.  An  Apple//e,  //c,  or  //gs  is
probably  required  with  the  Apple 80 column text card.  The VT100 keypad has
also been defined for the application mode via the OA/CA/game button.    Figure
1-1  shows  the  vt100  keypad  on an apple keyboard with EDIT (VMS) usage, and
Figure 1-2 shows the layout on an Apple//gs keypad.  When using EVE  (VMS)  the
meaning of the keys will of course change.

As  you  can see the keypad is physically laid out like the VT100 keypad except
for the lower right corner.  Notice that above the keys are  the  VT100  labels
while  in  middle of the box (key) is the Apple key label.  Also the arrow keys
work as VT100 arrow keys with the OA/CA/game button.


VT52 Emulation

SET TERMINAL VT52 will turn on the VT52 terminal emulation.  One thing that  is
required  is  your  80-column  card  must  handle  the $16 command in order for
reverse scrolling to work.  The Apple//e 80 column card handles this fine.  The
VT52  keypad  has  been defined using the open/closed Apple.  For II or II+ one
will have to have a game paddle or joy stick (key shift mod too????)   and  use
the  buttons.  When a button/open/closed Apple is pushed then the keys starting
with 6,7,8 & 9 form the top of the keypad. Key 6 is the blue key key 7  is  the
red  key etc. The keys directly below the 6,7,8 & 9 and shifted one-half key to
the right form the second row of the keypad etc. Every thing is fine until  you
get to the last row on the keypad. There the sp bar is 0 and the other two keys
are moved to the upper right as the 0 & - keys.  This way the  arrow  keys  are
available  as  VT52 keys with the OA/CA/game button combination (thanks to Dick
Atlee for this idea).  With those  two  exceptions  the  keypad  is  physically

1.5.15. The SET Command                                                 Page 18

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



                       PF1     PF2     PF3     PF4     .(period)
                     ------- ------- ------- ------- -------
                    |       |       |findnxt|delline|select |
                    |   6   |   7   |   8   |   9   |   0   |
                    | gold  | help  | find  |undelln| reset |
                     ------- ------- ------- ------- -------
                          7       8       9       -
                        ------- ------- ------- -------
                       | page  |section|append |delword|
                       |   Y   |   U   |   I   |   O   |
                       |command| fill  |replace|undelwd|
                        ------- ------- ------- -------
   vt100 key ---->            4       5       6       ,
                           ------- ------- ------- -------
   vms edit usage ---->    |advanc|backup |  cut  |delchar|
   apple key ---->         |  H   |   J   |   K   |   L   |
   vms edit usage ---->    |bottom|  top  | paste |undelch|
                           ------- ------- ------- -------
                                1       2       3       ENTER
                              ------- ------- ------- -------
                             | word  |  eol  | char  | enter |
                             |   N   |   M   |   ,   |   .   |
                             |chgcase|deleol |specins|  sub  |
                              ------- ------- ------- -------
                                    0
        ---------------------------------------
                                    bline      |
             space bar                         |
                                   openline    |
        ---------------------------------------

                Figure 1-1:  VT100 Keypad on an Apple Keyboard

-------------------------------------------------------------------------------

similar  to  a  VT52 keypad.  Remember the open/closed Apple or the game button
must be pushed (like the control key) to get the keypad emulation.  Figure  1-3
should clear up the questions.


1.5.16. the SHOW command

Syntax: SHOW [option]

The SHOW command displays various information:

    ALL                     All parameter settings (this is quite long).

    BAUD                    Baud rate of the com card.

    APPLICATION-MODE        Keypad in application mode?

    CLEAR-SCREEN            Clear screen on return from connect?

1.5.16. the SHOW command                                                Page 19

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



                       PF1     PF2     PF3     PF4
                     ------- ------- ------- -------
                    |       |       |findnxt|delline|
                    | CLEAR |   =   |   /   |   *   |
                    | gold  | help  | find  |undelln|
                     ------- ------- ------- -------
                       7       8       9       -
                     ------- ------- ------- -------
                    | page  |section|append |delword|
                    |   7   |   8   |   9   |   +   |
                    |command| fill  |replace|undelwd|
                     ------- ------- ------- -------
   vt100 key ---->      4       5       6       ,
                     ------- ------- ------- -------
   vms edit usage ->| advanc|backup |  cut  |delchar|
   gs key ------->  |   4   |   5   |   6   |   -   |
   vms edit usage ->| bottom|  top  | paste |undelch|
                     ------- ------- ------- -------
                       1       2       3       ENTER
                     ------- ------- ------- -------
                    | word  |  eol  | char  |       |
                    |   1   |   2   |   3   |       |
                    |chgcase|deleol |specins|       |
                     ------- ------- -------| enter |
                            0          .    | ENTER |
                     -----------------------|  sub  |
                    |    bline      |select |       |
                    |      0        |   .   |       |
                    |  openline     | reset |       |
                     -------------------------------

                   Figure 1-2:  VT100 Keypad on an Apple//gs

-------------------------------------------------------------------------------

    CURSOR-KEYS-VT100       Are  the  cursor  keys  emulating  the VT100 cursor
                            keys?

    DEBUGGING               Debugging mode.

    DEFAULT-DISK            Which Diskette drive is used for file transfer?

    DEVICE-DRIVER           Which communication device is being used?

    DISPLAY                 Which screen display is being used?

    ESCAPE                  Character for terminal connection.

    FILE-TYPE               Of Apple DOS/PRODOS file being sent/received.

    FILE-WARNING            Warn users if incoming file exists?

    FLOW                    Should XON/XOFF flow control be used to the remote?

1.5.16. the SHOW command                                                Page 20

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



    ^ is up arrow    BLUE     RED     GRAY     ^    .(period) ENTER
                     ------- ------- ------- ------- ------- -------
                    |       |       |delline|  up   |select | enter |
                    |   6   |   7   |   8   |   9   |   0   |   -   |
                    | gold  | help  |undelln|replace| reset |  sub  |
                     ------- ------- ------- ------- ------- -------
      v is down arrow     7       8       9       v
                        ------- ------- ------- -------
                       | page  |findnxt|delword| down  |
                       |   Y   |   U   |   I   |   O   |
                       |command| find  |undelwd|section|
                        ------- ------- ------- -------
       vt52 key ---->         4       5       6       ->
                           ------- ------- ------- -------
    vms edit usage ---->   |advanc|backup |delchar| right |
       apple key ---->     |  H   |   J   |   K   |   L   |
    vms edit usage ---->   |bottom|  top  |undelch|specins|
                           ------- ------- ------- -------
                                1       2       3      <-
                              ------- ------- ------- -------
                             | word  |  eol  |  cut  | left  |
                             |   N   |   M   |   ,   |   .   |
                             |chgcase|deleol | paste |append |
                              ------- ------- ------- -------
                                   0
        ---------------------------------------
                                    bline      |
             space bar                         |
                                   openline    |
        ---------------------------------------

                 Figure 1-3:  VT52 Keypad on an Apple Keyboard

-------------------------------------------------------------------------------

    KEYBOARD                II+ or //e keyboard.

    LOCAL-ECHO              Full or half duplex switch.

    LOG                     Are we logging connect data?

    PARITY                  Character parity to use

    PREFIX                  Which default prefix to use with PRODOS? Alias PWD.

    PRINTER                 Should the printer be used for the display?

    PROTOCOL                Which protocol is to be used for file transfer.

    RECEIVE                 Various parameters for receiving files

    SEND                    Various parameters for sending files

1.5.16. the SHOW command                                                Page 21

-------------------------------------------------------------------------------
    SLOT                    Which slot # is communication device in?

    SWAP                    Swap the del and backspace keys?

    TIMER                   Is the receive timeout on or off?

    TIMING                  Count for timing loop

    TERMINAL                Which terminal (if any) should Kermit emulate?

    VOLUMES                 Show the online volumes.

The above options are analogous to the equivalent SET commands.


1.5.17. The STATUS Command

Syntax: STATUS

Give statistics about the most recent file transfer. This includes  information
such   as  number  of  characters  sent/received,  number  of  data  characters
sent/received, and last error encountered.


1.5.18. The TAKE Command

Syntax: TAKE filespec

The TAKE commands tells kermit-65 to execute commands from the  specified  file
similarly  to  the  KERMIT.INIT  file.  See discussion on KERMIT.INIT above for
details.


1.5.19. The TYPE Command

Syntax: TYPE filespec

The TYPE commands tells kermit-65 to print to the  screen  from  the  specified
file. Text files only and works best with 80 characters per line or less.


1.5.20. The UNLOCK Command

Syntax: UNLOCK filespec

UNLOCK will unlock the given filespec on the default drive.


1.6. Installation

1.6.1. Standard Installation                                            Page 22

-------------------------------------------------------------------------------
1.6.1. Standard Installation

To  bootstrap  Kermit  to  prodos, get the file APPPRO.BNS on a apple diskette.
Use binscii to convert this file into a shrinkit file. Use shrinkit to  extract
the  files  onto a prodos diskette with your own prodos and basic.system files.
Then "-read.me" for further instructions. Thanks to Les Ferch for this  install
system & thanks to Bird for his "birds better bye" in the menu.system.  For dos
3.3 get the files APP387.[1-2] on a master diskette  then  read  the  first  of
app387.1 for further instructions.  Thanks to Alan Kalker for this install sys-
tem.

The kermit binaries will run on either system.  Simply use the  PRODOS  conver-
sion  routines (if they have them fixed, better to use copy II+ or whatever) to
move kermit, kermit.help and kermit.init files.  If you want other options as a
regular thing then you can change file kermit.init with your favorite editor.


    Files Supplied for Kermit-65

The following files should be supplied on the columbia distribution tape:

    APP387.1       Install system for dos 3.3 (1 of 2)
    APP387.2       Install system for dos 3.3 (2 of 2)
    APPAAA.HLP     List of files (like this one)
    APPAAA.NEW     Whats new in this release
    APPACC.HEX     Apple com card hex
    APPACC.M65     Apple com card source
    APPACE.HEX     Ace dual card hex
    APPACE.M65     Ace dual card source
    APPBEL.BNS     Apple gs alternate bell
    APPCAT.HEX     Apple cat hex
    APPCAT.M65     Apple cat source
    APPCCS.HEX     CCS 7710 com card hex
    APPCCS.M65     CCS 7710 com card source
    APPCPS.HEX     CPS com card hex
    APPCPS.M65     CPS com card source
    APPGS.HEX      GS serial port hex
    APPGS.M65      GS serial port source
    APPHMM.HEX     Hayes micro modem card hex
    APPHMM.M65     Hayes micro modem card source
    APPICON.BNS    Kermit icon for gs users
    APPLE.DOC      Complete documentation (it says here)
    APPLE.MSS      Scribe text formatter source for documentation
    APPLE.PS       Documentation ready for a postscript printer
    APPMAI.HEX     Main kermit pgm hex
    APPMAI.M65     Main kermit pgm source
    APPMAK.UNX     Make file for UNIX cross assembly (to assemble Kermit)
    APPMSV.HEX     Microtec com card hex
    APPMSV.M65     Microtec com card source
    APPPRO.BNS     Install system for prodos
    APPSSC.HEX     Super serial com card hex
    APPSSC.M65     Super serial com card source
    APPXAS.1       65c02 cross assembler for UNIX system part 1
    APPXAS.2       65c02 cross assembler for UNIX system part 2
    APPXAS.3       65c02 cross assembler for UNIX system part 3

1.6.1. Standard Installation                                            Page 23

-------------------------------------------------------------------------------
The  syntax  of the filenames may vary.  On UNIX systems, the filenames will be
in lowercase.  On VM/CMS systems, the period will be replaced by a space.   All
files are text, however the suffix of BNS are binsciied binary files.


1.6.2. Alternate Installation

The  main  problem exists in getting the hex files onto your diskette as a text
file.  But again that is a test of your creativity. If you have  a  version  of
Kermit running then GET or RECEIVE the file as a text file and you are in busi-
ness.  Since Kermit has been separated into two assemblies then two  hex  files
will  have  to be present on the diskette. Get the main hex file APPMAI.HEX and
select which com card hex you will need. First "exec APPMAI.HEX".   Your  Apple
(or  compatible)  will  go  into  monitor and show you *'s for several minutes.
This is the monitor loading the hex into binary.  If you  get  beeps  from  the
monitor  its probably because you didn't get a good copy of the text file.  Now
EXEC the com card driver you are going to use.  You will have to get back  into
basic(aha  another  test for you, try "3d0G") to do this.  And you will see the
monitor loading the com driver. The order of EXEC's is important.  The com card
should   be   loaded  last.    Next  get  back  into  basic  and  do  a  "bsave
kermit,A$1000,L$7000".  You may have to specify the drive  to  do  this  binary
save, with a slot or drive on the end of the BSAVE (aha another test).  You now
run Kermit via "brun kermit".

If you want to customize Kermit for your needs, the recommended  method  is  to
use  file  "kermit.init"  OR do all your SETs, etc, and then do an "exit".  Now
you should be back in BASIC.  At this point do a "bsave name,A$1000,L$7000" and
when  you  do  a  "brun name" all your setups will be remembered.  NOTE: If you
save your current settings via "bsave kermit ..." you may find that moving that
binary  to  another type of Apple (e.g. from a //e to an //e+) will not be pos-
sible.  So make sure you keep the  original  binary  to  move  between  machine
types.

Since  the org is now $1000 if you have been using Kermit and then went back to
basic for some trivial thing a "CALL  4096"  should  start  up  Kermit  without
having to reload it.

In summary:

   1. EXEC APPMAI.HEX

   2. Choose the com card driver you will use.  For example APPSSC.HEX.

   3. 3D0G

   4. EXEC APPSSC.HEX

   5. BSAVE kermit,A$1000,L$7000

And you should be in business.  Remember there is the command HELP and whenever
you are into a command a "?" will give you the possible  options  available  at
that  point of a command.  The escape key will finish typing an option if it is
possible. The syntax of all the  commands  and  options  only  requires  enough
characters to make that command or option unique.

1.7. Problems                                                           Page 24

-------------------------------------------------------------------------------
1.7. Problems


    Installation

NOTE:  When  using  the  super  serial driver you must have the cards sw6-2 on.
This allows the card to use interrupts. The rest of the switches are  set  from
within  Kermit.  It  appears that you can run your Apple 2 with sw6-2 on and in
99% of the cases will cause no problems.  This is because the OS runs with  in-
terrupts  locked  out  ("sei"  in  assembly  language) and the program must ex-
plicitly give a "cli" for interrupts to work (the super serial driver does).

The AE Serial Pro must have switches 1 & 3 open and 2 & 4 closed. This  appears
to disagree with the documentation since those settings turn off irq interrupts
and turn on nmi interrupts. So watch this it may get corrected  in  later  ver-
sions.

The Microtek driver is a super serial look alike which does not run with inter-
rupts.  If you have trouble with the super serial driver you might try the  MSV
driver.   For you people with the MSV-622c card, you might try running a jumper
from the UART 6551 pin 26 to the card edge pin 30.  This will enable interrupts
just like the SSC sw2-6, and then you can use the super serial driver.

The Prometheus card will work with the Apple com driver.  However you will have
to set the switches on the card for baud etc.  Evidently this card can  not  be
programmed by the software. If that is not true then here is an opportunity for
you to write a better driver. If you do please pass it on for other  Prometheus
users.

The  apple  cat  uses the modem's firmware for dialing. Type ";" for a 2 second
delay, or any control character to abort the dialing. ROM is not needed if  ex-
ternal  phone  is  used for dialing.  Supports 110-600 baud, and 45.5 baud (use
kermit-65's 135 baud setting).  Supports 1200 baud with apple-cat 212 card,  in
slot-saver  configuration.  Allows use of external serial port by typing "X" as
dialing string.  Thanks to Dick Wotiz for this driver.  Reports  have  it  that
the Apple Cat will also work with the Apple com driver.

Some  have  noted  the Apple com card must be initialized via the "IN#x" before
starting Kermit. Ike has now updated this driver and the initialization is  now
done within the Apple com driver.  Thanks Ike.


    Usage

There  is the command HELP and whenever you are into a command a "?"  will give
you the possible options available at that point of a command. The  escape  key
will  finish typing an option if it is possible. The syntax of all the commands
and options only requires enough characters to  make  that  command  or  option
unique.

When  using flow control you may appear to hang. Type a ^Q (Control-Q) and that
may free you up.

Remember when you use your printer there are a lot of variables here.  What was
being  sent  to  the  screen  now  is  being sent to your printer.  If you were
emulating the VT52 your printer may not know  how  to  handle  the  escape  se-

1.7. Problems                                                           Page 25

-------------------------------------------------------------------------------
quences,  tabs  etc. It may be you can tell the host you are a tty or some such
device that will give carriage returns etc that your printer can handle.   Some
printers may require the flow control and delay to get readable printing.


    File Transfer Errors

"File  Transfer  Errors,"  was added to this document by the Southeast Regional
Data Center (SERDAC), '88 July 17.

In spite of the fact that successful Kermit file transfers  are  almost  always
error  free, there are a number of circumstances which can corrupt, prevent, or
interrupt/abort a transfer.  In the case of an actual abort, there may be  data
loss  or corruption, and an incomplete file may not have a correct end-of-file.
These circumstances may be roughly divided into two groups: (1) problems due to
file  or  disk  errors,  and  (2)  problems due to delays or failures in Kermit
packet exchange.

Common problems in category (1) include the following:

(a) improper file specification (b) wrong file type (c) protected  file(s)  (d)
disk problems

(1a) problems can occur when you specify, to either the Apple or host Kermit, a
non-existent  or  improperly  located  file.    Misspelling  and/or   incorrect
(sub)directory  specification  are popular villains!  If you are commanding ei-
ther Kermit to SEND a file (SEND filespec), the problem will be fairly obvious.
On  the  Apple  II, you'll see an error message like: "FILE NOT FOUND."  On the
VAX/VMS 8800, for example, you'll see the message: "%KERMIT32 .....,  file  not
found  for  'filespec'".  In either case, the transfer will not take place.  If
you're using Kermit-65 to GET (GET filespec)  files  from  the  VAX/VMS  Kermit
server,  and  the  requested file does not exist in your VAX default directory,
you should see a Kermit-32 generated "REMOTE MESSAGE %KERMIT32 ....., file  not
found  for  'filespec'" appear in the transmission status display, and then the
Kermit-65 message "CANNOT RECEIVE FILE-HEAD".   Transfer  of  the  questionable
file will not take place.

(1b)  problems  can occur if you forget to specify, to either the Apple or host
Kermit, what type of file you wish to transfer.  If you are using Kermit-65  to
send files to a host, you are fairly well protected against this error.  If you
attempt to send a  file  whose  CATALOG  type  does  not  match  the  FILE-TYPE
parameter setting, you will receive a "INCOMPATIBLE FILE FORMAT" error message,
or something similar, and the transfer will not take place.  If,  however,  you
are  receiving (via RECEIVE or GET) a file whose native type does not match the
FILE-TYPE setting, the file WILL be received.  It will be mis-typed  (according
to the FILE-TYPE setting), though, and any later attempt to use it on the Apple
will probably be unsuccessful.

The same sort of circumstances generally apply for a host Kermit. With the  VAX
8800,  for  example,  when  Kermit-32 is sending a file, you generally need not
worry about setting its file  type.    When  Kermit-32  is  receiving  a  file,
however,  properly  setting its file type is very critical.  If you wish to put
Kermit-32 in server mode to receive multiple files, set the  file  type  BEFORE
using  the  SERVER command, and make sure that you only send it the appropriate
type of files during that server session.  You cannot switch file types  DURING
a given server session!

1.7. Problems                                                           Page 26

-------------------------------------------------------------------------------
NOTE:  One other way you can get into trouble with "wrong file type" is by try-
ing to send a file which is mixed-- mostly text, but with some embedded charac-
ters that are not true 7-bit ASCII (i.e., ASCII codes 00-127).  This often hap-
pens when you are trying to transfer a file which  is  word  processor  output.
Most  word  processing  software  claims to allow you to output a true ASCII or
text file, but in some cases it really does not, and in others  the  choice  of
output  options  is  confusing.    If  you have set up either Kermit program to
send/receive a text file, and you try  to  transfer  illegal  ASCII  characters
(codes  128-256), your transfer may "hang" or be aborted.  At the very best, if
the transfer "works," the suspect characters will later probably be meaningless
or confusing to the destination machine.

(1c)  problems  can  occur  in two ways on the Apple II.  If your default drive
disk is write protected, and you attempt to receive a file, you will receive  a
"WRITE  PROTECTED" error message, and no transfer will take place.  If you have
set Kermit-65's FILE-WARNING parameter to OFF (normally NOT a good  idea),  and
you  attempt  to  receive  a file that already exists in a locked state on your
default diskette, you will receive a "FILE LOCKED" error message (if  the  file
is very short, you may have to check with a Kermit-65 STATUS command to see the
error message), and no transfer will take place.

Similar problems may occur on the  host  because  of  various  file  protection
schemes.    On  the VAX/VMS 8800, for example, Kermit-32 cannot send out a file
that you are unauthorized to read.  And, it cannot receive a  file  unless  you
are  authorized  to  write to that filename and its (sub)directory.  If you use
Kermit-32 to attempt to SEND (SEND filespec) a protected file, you should see a
"%KERMIT32  .....,  insufficient  privilege  or  file  protection violation for
'filespec'" error message, and no transfer  will  take  place.    If  you  have
Kermit-32  in  server mode, and you are trying to GET a protected file from it,
or you are trying to SEND it a file whose space is protected, you should see  a
similar  Kermit-32  generated  REMOTE MESSAGE appear in the transmission status
display, and then, on GET, the Kermit-65 message  "CANNOT  RECEIVE  FILE-HEAD".
Transfer of the protected file will not take place.

(1d)  problems  are  most likely to occur because of Apple II diskette or drive
problems.  The following conditions will generate "DISK  I/O"  or  "I/O  ERROR"
messages when Kermit-65 transfer commands are entered:  bad diskette in default
drive, no diskette in default drive, default drive door open, and/or unINITial-
ized disk in default drive.

If  any  of  those  errors  are detected before the attempted transmission of a
given file, the transfer of that file will  not  begin.  If  any  are  detected
DURING a file transmission, the file transfer will likely abort; at best trans-
mitted data will be incomplete. Data which does reach the destination end of an
aborted  transfer should be considered very suspect; the disk problem should be
corrected and the transfer should be repeated!  (The best chance you  have  for
salvaging  text  file  data  in an abort is if the file destination is the host
machine and you have told its Kermit to save incomplete  files,  e.g.,  on  the
VAX-8800, you need to SET INCOMPLETE KEEP).

One  other  Apple  II  disk  problem  can  be  encountered  while you are using
Kermit-65 to receive files. If you exceed the storage capacity of your diskette
during  a  RECEIVE  or a GET, you should see a "DISK FULL" error message.  Data
that has been received up to the point of the overflow  will  be  automatically
DELETEd.   Make CERTAIN that you do not try to receive any more files until you
have DELETEd some files from the problem diskette, or until you  have  replaced

1.7. Problems                                                           Page 27

-------------------------------------------------------------------------------
it with one that has adequate capacity to receive the complete file.  NOTE: See
Section 1.5.4.

It is less likely that (1d) problems would occur because of host  machine  disk
problems.    The  most  likely  circumstance you might encounter on the VAX/VMS
8800, for example, would be in receiving a large file and, in the process,  ex-
ceeding  your  VAX  disk  quota.  In such a case, you should see an appropriate
Kermit-32 generated REMOTE MESSAGE appear  within  the  Kermit-65  transmission
status   display.      If  this  happens,  delete  some  files  from  your  VAX
(sub)directories, and/or have your VAX disk quota increased BEFORE you try  the
transfer  again. If you have issued a SET INCOMPLETE KEEP command to Kermit-32,
there may be some chance of salvaging text file data that  arrived  before  the
disk quota overage, but the best thing you can do is to repeat the transfer!

As  a  general rule, if some disk or file error prevents a transfer from begin-
ning, to get it to "go," you will need to correct the error and repeat all  the
steps that preceded it.

If  you are still commanding the host Kermit, and you see an error message, you
will have to get the host Kermit's prompt back and give it an  acceptable  com-
mand.  If  you  have commanded the host Kermit to SEND or RECEIVE, and are back
commanding Kermit-65 when you notice the error, you will have  to  correct  the
problem, CONNECT back to the host, get the host Kermit prompt (with the VAX/VMS
8800, try typing RETURN or CTRL-Y), and repeat the SEND or RECEIVE command, be-
fore returning back to Kermit-65 to command it again.

If  you  have  placed  the host Kermit in server mode, and are giving Kermit-65
commands when you notice an Apple disk/file error prevents a file transfer from
starting, chances are good that you won't have to CONNECT back to the host.  It
is also important to note that within a single server  session,  when  you  are
transferring  multiple  files,  all  files  transferred  PRECEDING an error (or
abort) are probably good. To repeat the transfer, correct the error,  and  give
Kermit-65  the  appropriate  command  to  transfer the file that messed up. The
first time you do  it,  you  may  get  back  a  message  like  "REMOTE  MESSAGE
%KERMIT-32..... protocol error" This is just the host server trying to get back
"on track" after the error.  When the  Kermit-65>  prompt  returns,  enter  the
transfer command again, and it will probably be accepted.

If  the  second  attempt  should  fail,  wait for the Kermit-65> prompt, enter:
FINISH, wait for the prompt again, and enter: CONNECT.  If you do not  see  the
host operating system prompt ($ on the VAX 8800), type a few RETURNs (or on the
VAX/VMS a CTRL-Y). Re-invoke the host Kermit and put it back in server mode.

If disk or file errors prevent a transfer from completing, recovery will depend
on  the  error,  whether  you had the host Kermit in server mode or not, and on
your desire for accuracy.

Some disk/file error aborts are "fatal" (e.g., Apple DISK FULL,  and  uploading
to  the  VAX  8800 w/o having commanded Kermit-32 to SET INCOMPLETE KEEP).  The
destination file will be destroyed.  The transfer of the file will have  to  be
repeated  again from the beginning.  Again, unless you have set the host Kermit
for server mode, you will have to CONNECT back, get the host Kermit prompt, and
re-command  it.    If  you  were  in a server session, though, you can probably
repeat the transfer of the interrupted file without going back to the host (see
recovery procedures above).

Other  disk/file  errors  that interrupt/abort a transfer may leave salvageable

1.7. Problems                                                           Page 28

-------------------------------------------------------------------------------
text data at the transfer destination.  The best policy, though, is  to  repeat
the transfer of the incomplete file (see recovery procedures above).

Common problems in category (2) include the following:

(a) bad parity

(b) noisy communications line

(c) timeout due to delays, "disaster," etc.

(d) Kermit-program incompatibility

(e) user error

(2a)

Parity  settings  are very critical to correct transfers.  If you do not inform
Kermit-65 of the correct parity being used by the remote host  machine  or  the
communications  path  to  it,  "checksum"  error  checking calculations will be
wrong, and packets will be consistently rejected when they arrive at their des-
tination.   In particular, most binary file Kermit transfers won't get very far
if parity is not set correctly.

[NOTE: If you want to do a binary file transfer (Apple binary or  BASIC  files)
via  a  FIRN Network connection to the SERDAC VAX/VMS 8800, you must SET PARITY
SPACE before the transfer is initiated; that will insure that eight-bit quoting
is  used.    If  you  dial  directly  into  the  VAX/VMS 8800, SET PARITY NONE;
eight-bit quoting (which is less efficient) is not required].

(2b)

Line noise can be the root cause for a variety of file transfer problems.   The
beauty  of  a  "packetized  protocol  transfer"  scheme like Kermit is that or-
dinarily, the scheme will overcome an occasional burst of line noise.  A packet
which  arrives  out  of sequence, or which does not have the same checksum "bit
count" as when it was sent, will get retransmitted, and the noise induced  data
error will correct itself.

Sometimes,  however,  bad  line  noise can outwit even the cleverest aspects of
Kermit.  There are some times where severe noise can corrupt the "checksum" er-
ror  checking  and lead to undetected transmission of a bad character (assuming
that the severe line noise exists, chances of this happening for one  character
are, for Kermit-65 error checking, less than two percent).

If  line  noise  is  bad  enough  and persistent enough, it is also a cause for
several problems that will eventually "hang" or totally  confuse  and  abort  a
transfer:

Each  transfer  is  preceded  by the Kermit-to-Kermit exchange of several short
"initialization packets.  These tell the controlling programs  critical  things
to  expect about the upcoming transfer. If line noise prevents the packets from
arriving, or scrambles them up, the transfer probably can't  get  started  cor-
rectly.

One  of  the biggest vulnerabilities of the Kermit scheme is that each arriving

1.7. Problems                                                           Page 29

-------------------------------------------------------------------------------
packet must be acknowledged (ACK) by the receiver, and that the sender must ac-
tually  receive  back the acknowledgement (likewise, if an expected packet does
not arrive, there often must be a negative acknowledgement (NAK)).   Since  the
ACK/NAK packets are very short, they are rather vulnerable to severe noise.  If
too many of them are scrambled or lost, the transfer can get out of synch,  and
the transferring programs can lose track of where they are.

One other place Kermit is vulnerable is in the beginning of a data packet.  The
first several bytes of these longer packets are  reserved  for  control  infor-
mation:  packet  type,  byte  count,  sequence  number,  etc.    If  line noise
repeatedly coincides with the transmission of this control information,  it  is
very easy for the transfer to get confused-- particularly if the packet number-
ing gets garbled.

If you detect frequent line noise after you've connected to a host, but  before
you begin transfers (you will probably see extraneous junk characters appearing
on your screen), you're probably in for trouble. Once transfers actually begin,
line  noise  problems  are  often  characterized  by  incrementing of the RETRY
counter on the Kermit-65 transmission status display, and/or by long pauses  in
incrementing of the status display byte counter.

To minimize line noise, first see if there are any obvious loose connections in
your equipment (telephone line connection to wall box, telephone line to modem,
modem  cabling  to  serial connector, or, if appropriate, cabling from hardwire
port to serial connector).  If not, you may want to hang up and redial  to  get
another  telephone  connection  (almost every connection is unique, and you may
get a better one than you had).  Many line noise problems will  clear  up  with
those simple remedies, but some may be beyond your control!

If  all else fails, you may also try shortening the maximum length of your data
packets (SET SEND/RECEIVE PACKET-LENGTH) to possibly lessen the effects of per-
sistent noise.

(2c)

A Kermit transfer consists of a regular and predictable exchange of initializa-
tion, data, and, ACK/NAK packets.  If something  (line  noise,  busy  computer,
user  error,  etc.) interrupts or delays this regular exchange, there must be a
way for a Kermit program on at least one end to figure out something  is  wrong
and try to get the packet exchange back on track again.

This  is  usually  done with a timer and retry mechanism.  If a Kermit does not
receive an expected packet, within its timer's time limit (a timeout), it  will
resend  its  last sent packet to try to "wake up" the other Kermit (effectively
by asking it to send its last  packet  again).    This  resending  is  repeated
("retried")  a  number of times before the program assumes it cannot get things
on track again.  Each packet resent by Kermit-65 is counted as a RETRY  on  its
transmission status display. If Kermit-65's retry count exceeds 20, it will try
to issue an error message according to what kind of packet it was  waiting  for
and/or it will say MAX RETRY COUNT EXCEEDED. The transfer will then be aborted.

Very  frequently,  timeouts  are caused by unexpected delays in the remote com-
puter, or in the network thru which you connect to it.  If you  know  that  the
host machine or network is very busy, and you repeatedly have aborted transfers
due to timeouts, you may be able to alleviate the  problem  by  increasing  the
value of the default Kermit-65 receive timeout parameter (SET RECEIVE TIMEOUT).

1.7. Problems                                                           Page 30

-------------------------------------------------------------------------------
Other  common  ways  that  Kermit-65 can timeout and abort are: (1) if the host
machine "goes down" during a  transfer,  (2)  if  the  telephone,  network,  or
hardwire  connection  is completely broken during a transfer, (3) if you forgot
to "start up" the host Kermit and give it a transfer command (SEND, RECEIVE, or
SERVER)  BEFORE  giving  Kermit-65  a  transfer command, and (4) if (2a), (2b),
(2d), or (2e) problems occur and  critical  initialization  packets  are  never
received.

In cases (1) and (2), you will eventually probably see a CANNOT RECEIVE DATA or
MAX RETRY COUNT EXCEEDED message from Kermit-65.  Cases (3) and (4) may  result
in a CANNOT RECEIVE INIT message.

(2d)

To  do  effective Kermit transfers, there must be two Kermit programs working--
one on either end of a "computer connection."  In  addition,  the  two  Kermits
must  be  able  to "talk to" each other in a prescribed, standard way. Although
there are specific standards for writing all Kermit programs, most of them have
been  written  by  volunteers and are in the "public domain."  The protocol re-
quirements and resultant programs are generally rather complex, and it  is  all
too  easy to inadvertently program in a subtle error in a given Kermit version.
Additionally, there are many "levels of ability" of Kermit programs:  some  can
operate  in server mode, some cannot. Some can transfer binary files; some can-
not, etc.  Unless the Kermit programs you are using are both  error  free,  and
both  have the same capabilities for the transfers you wish to perform, you are
in trouble!

If there is a systematic "bug" in one of the Kermit programs, or if you are as-
king  one  Kermit  to  do something the other can't do, there will usually be a
problem with packet exchange; in many cases the  requested  transfer  will  not
even  get  started.  You may see a Kermit-65 error message, on the transmission
status display, saying that a packet was not received, or a REMOTE MESSAGE say-
ing  a  packet was unexpectedly received, or one that the command cannot be ex-
ecuted by the other Kermit.  In some cases, you may see  no  explanatory  error
messages  at  all;  the  transfer will just "hang" and will probably eventually
"timeout" and abort (MAX RETRY COUNT EXCEEDED).

(2e)

If you've read about category (1) errors above, you can see that  there  are  a
variety  of things you can do to with files or disks to mess up a Kermit trans-
fer.  You can also wreak havoc by issuing improper or illegal commands to  Ker-
mit  programs.    Before trying to transfer a lot of files, or trying out a new
type of transfer, be sure you understand the procedure you need to  follow  and
the various Kermit commands that will be involved.

New  Kermit  users  often  try  to  command  their  local Kermit program (e.g.,
Kermit-65) to send or receive a file, without having  first  invoked  and  com-
manded the host Kermit.

Another common error is to issue improper commands to a remote server.  For ex-
ample, when VAX/VMS Kermit-32 is in server mode, and you are  requesting  files
from  it via Kermit-65 commands, you cannot use a RECEIVE command; you must in-
stead use GET.

As with Kermit program incompatibilities,  illegal  or  inappropriate  commands

1.7. Problems                                                           Page 31

-------------------------------------------------------------------------------
will  often  cause  a problem with packet exchange; in many cases the requested
transfer or action will not even get started.  You may see  a  Kermit-65  error
message,  on the transmission status display, saying a packet was not received,
a REMOTE MESSAGE that a packet was unexpectedly received, or one that the  com-
mand cannot be executed by the other Kermit.  In some cases, you may see no ex-
planatory error messages at all; the transfer will just "hang" and  will  prob-
ably eventually "timeout" and abort (MAX RETRY COUNT EXCEEDED).

Except  for  the  fact that you will probably never note a category (2) "packet
exchange" error while you are "talking to" the remote system or commanding  its
Kermit,  and  that  the  remedies you must employ to correct the errors will be
different, recovery procedures to get your file transferred correctly  will  be
much  the  same  as those we described at the end of the discussion on category
(1) "disk/file" errors.  Make sure to read that  discussion  for  more  details
than we have included below.

In  short,  if  an error prevents a given transfer from actually beginning, you
will need to correct the error and repeat all the steps that preceded it.  This
will be more difficult if you are transferring only one file-- having commanded
the remote Kermit to SEND or RECEIVE.  If you have placed the remote Kermit  in
server  mode,  and an error prevents the transfer of one file, all files trans-
ferred up to that point are probably  OK,  and  you  can  usually  correct  the
problem,  and  get a transfer started again without having to reCONNECT back to
the host.

If you are transferring a text file, and an abort occurs in mid-transfer,  some
data  may  be  salvageable  in the destination file, but the best rule with any
type of file is to repeat the transfer, in which case the  recovery  procedures
in the last paragraph apply.


1.8. Customizing Kermit-65

The  source code to Kermit-65 is in 6502 Assembler. It has been formatted for a
cross assembler which runs on a unix 2's complement machine.    Files  appxas.1
thru appxas.3 are the cross assembler for UNIX.  Get the files on a UNIX system
and then look at the documentation at the start. They will easily  make  you  a
xasm  for  Kermit.  The file appmak.unx is the makefile to use with the xasm to
reassemble all of Kermit's parts.

Kermit-65 has been separated into two assemblies, the main routines and the com
card  routines for the devices shown in Table 1-1.  A vector has been set up in
low memory for the two assemblies to  communicate.  Look  at  the  working  com
drivers  for  tips  on  how to incorporate your version of the com driver. some
things to note: It is probably best to buffer the input from the remote and  to
get  input  characters from the remote every chance you get.  Note the Microtek
SV-622 driver, whenever the input is checked for a character and has a  charac-
ter  the character is put into the buffer immediately.  Also when the output is
checked for ready to output, if the card is not ready  to  output  then  it  is
checked  for a character to input.  All this should help prevent losing charac-
ters.

All the routines should return with the "rts" instruction.  Routines which  can
return  a  true/false indication should return with the P reg zero flag set ap-
propriately.  That is: a "beq" instruction will branch on  a  false  indication
and  the  "bne"  will branch on a true indication.  The com driver should start

Apple II Kermit                                                         Page 32

-------------------------------------------------------------------------------
its routines above the main routines and tell where the end of the  com  driver
is  via  location  $100c.  If your com driver gets too large then the bsave ad-
dress would have to be changed when you are saving the binary to diskette.

Apple II Kermit                                                         Page 33

-------------------------------------------------------------------------------
  address size  module   function
  1003    byte   main     This is the baud rate index as follows:
                           3 - 110
                           4 - 135.4
                           5 - 150
                           6 - 300
                           7 - 600
                           8 - 1200
                           9 - 1800
                          10 - 2400
                          11 - 3600
                          12 - 4800
                          13 - 7200
                          14 - 9600
                          15 - 19200
                          eg:if index is 6 then line should be 300 baud
  1004    byte            unused
  1005    word   driver   Address of a null terminated string.
                          address should point to a capitalized
                          string of the drivers id
  1007    byte   main     Com slot in the form $n0 where n is slot #.
  1008    byte   main     Force initialization flag when 0.
                          init routine should always initialize when
                          this flag is 0 & then set flag non-zero.
  1009    word   main     Address of the end of Kermit main routine.
  100b    byte   main     Flow control is on when high bit is set.
  100c    word   driver   Address of the end of the com driver.
  100e    byte   driver   Time constant-used with the 1040 rtn.
  100f    word   driver   Address of the end of screen save memory(//e).
  1011    byte   driver   Screen saved flag.
  1020  3 bytes  driver   Jump to initialization routine.
  1023  3 bytes  driver   Jump to command routine.  A reg has command
                            0 - hang up the line
                          $0b - set baud rate
                          $0c - set break on the line
                          $91 - do xon on the line
                          $93 - do xoff on the line
                          routine returns false (P reg zero flag) if unable
  1026  3 bytes  driver   Jump to check for input from the line.
                          routine returns false (P reg zero flag)
                          if no character on line
  1029  3 bytes  driver   Jump to get input character from line.
                          routine returns character in A reg
  102c  3 bytes  driver   Jump to put character in A reg on line.
  102f  3 bytes  driver   Jump to reset com driver.
  1040  3 bytes  main     Jump to Apple ROM wait rtn. microsecs delay
                          =1/2(26+27A+5A*A) where A is the accumulator
  1043  3 bytes  main     Jump to routine to print null-terminated string.
                          X reg contains least significant byte of address
                          Y reg contains most significant byte of address
                          routine does not issue a carriage return.
  1046  3 bytes  main     Jump to routine to read the keyboard.
                          A reg contains the character read
  1049  3 bytes  main     Jump to routine to print carriage rtn & line feed.
  104f  3 bytes  main     Jump to routine to set characters parity.
                          A reg contains the character before and after.

                  Table 1-4:  Communications card vector area

Apple II Kermit                                                         Page 34

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



              List of most of the prodos file types.

  Num      Name    OS      Definition
  $00                      typeless
  $01      BAD     both    BAD blocks file
  $02      PCD     SOS     Pascal CoDe file
  $03      PTX     SOS     Pascal TeXt file
  $04      TXT     both    ASCII text file
  $05      PDA     SOS     Pascal DAta file
  $06      BIN     both    BINary file
  $07      CHR     SOS     CHaRacter font file
  $08      PIC     both    PICture file
  $09      BA3     SOS     Business BASIC (SOS) program file
  $0A      DA3     SOS     Business BASIC (SOS) data file
  $0B      WPD     SOS     Word Processor Document
  $0C              SOS     SOS system file
  $0D              SOS     SOS reserved file type
  $0E              SOS     SOS reserved file type
  $0F      DIR     Both    subDIRectory file
  $10      RPD     SOS     RPS data file
  $11      RPI     SOS     RPS index file
  $12              SOS     Applefile diskcard file
  $13              SOS     Applefile model file
  $14              SOS     Applefile report format file
  $15              SOS     Screen library file
  $16              SOS     SOS reserved file type
  $17              SOS     SOS reserved file type
  $18              SOS     SOS reserved file type
  $19      ADB     ProDOS  AppleWorks Database file
  $1A      AWP     ProDOS  AppleWorks WordProcessing file
  $1B      ASP     ProDOS  AppleWorks Spreadsheet file
  $1C-$5F                  Reserved
  $60-$6F          ProDOS  PC Transporter (Applied Engineering)
   $60     PRE     ProDOS  ProDOS preboot driver
   $61-$6A         ProDOS  Reserved
   $6B     NIO     ProDOS  PC Transporter BIOS and drivers
   $6C             ProDOS  Reserved
   $6D     DVR     ProDOS  PC Transporter device drivers
   $6E             ProDOS  Reserved
   $6F     HDV     ProDOS  MSDOS HardDisk Volume
  $70-$9F                  Reserved
  $A0      WPF     ProDOS  WordPerfect document file
  $A1      MAC     ProDOS  Macrofile
  $A2      HLP     ProDOS  Help File
  $A3      DAT     ProDOS  Data File
  $A4                      Reserved
  $A5      LEX     ProDOS  Spelling dictionary
  $A6-$AB                  Reserved

                     Table 1-5:  PRODOS file types, part 1

-------------------------------------------------------------------------------

Apple II Kermit                                                         Page 35

-------------------------------------------------------------------------------
-------------------------------------------------------------------------------



  Num         Name    OS      Definition
  $AC         ARC     ProDOS  General Purpose Archive file
  $AD-$AF                     Reserved
  $B0         SRC     ProDOS  ORCA/M & APW source file
  $B1         OBJ     ProDOS  ORCA/M & APW object file
  $B2         LIB     ProDOS  ORCA/M & APW library file
  $B3         S16     ProDOS  ProDOS16 system file
  $B4         RTL     ProDOS  ProDOS16 runtime library
  $B5         EXE     ProDOS  APW shell command file
  $B6         STR     ProDOS  ProDOS16 startup init file
  $B7         TSF     ProDOS  ProDOS16 temporary init file
  $B8         NDA     ProDOS  ProDOS16 new desk accessory
  $B9         CDA     ProDOS  ProDOS16 classic desk accessory
  $BA         TOL     ProDOS  ProDOS16 toolset file
  $BB         DRV     ProDOS  ProDOS16 driver file
  $BC-$BE                     Reserved for ProDOS16 load file
  $BF         DOC     ProDOS  document file
  $C0         PNT     ProDOS  //gs paint document
  $C1         SCR     ProDOS  //gs screen file
  $C2-$C7                     Reserved
  $C8         FNT     ProDOS  Printer font file
  $C9                 ProDOS  finder files
  $CA                 ProDOS  finder icons
  $CB-$DF                     Reserved
  $E0         LBR     ProDOS  Apple archive library file
  $E1                         Unknown (unlisted)
  $E2         ATI     ProDOS  Appletalk init file
  $E3-$EE                     Reserved
  $EF         PAS     ProDOS  ProDOS Pascal file
  $F0         CMD     ProDOS  added command file
  $F1-$F8             ProDOS  User defined filetypes
                            (popular ones include:)
   $F1        OVL     ProDOS  Overlay file
   $F2        DBF     ProDOS  Database file
   $F3        PAD     ProDOS  MouseWrite file
   $F4        MCR     ProDOS  AE Pro macro file
   $F5        ECP     ProDOS  ECP batch file
   $F6        DSC     ProDOS  description file
   $F7        TMP     ProDOS  temporary work file
   $F8        RSX     ProDOS  linkable object module
  $F9         IMG     ProDOS  ProDOS image file
  $FA         INT     ProDOS  Integer BASIC program
  $FB         IVR     ProDOS  Integer BASIC variables file
  $FC         BAS     ProDOS  AppleSoft BASIC program
  $FD         VAR     ProDOS  AppleSoft BASIC variables file
  $FE         REL     ProDOS  ProDOS EDASM relocatable object module file
  $FF         SYS     ProDOS  ProDOS8 system file

                     Table 1-6:  PRODOS file types, part 2

-------------------------------------------------------------------------------

Apple II Kermit                                                         Page 36

-------------------------------------------------------------------------------
Index

          Apple II   1               Padding   16
          Apple II Keypad   17       Prodos file system   4
          Apple II+ keyboard   7     Prompting   6
          Applesoft   13
          Archiving files   3        Q   8, 10
                                     Quote-char   16
          Backspace key   16
          Binary   13                Readme   22
          Blink   7                  RECEIVE Command   10
                                     REMOTE Command   10
          CA key   17, 18            RENAME Command   10
          CATALOG Command   6        RM Command   8
          CD Command   15
          CONNECT Command   6        SEND Command   10
          Control-c   11             SERVER Command   11
          Cr-cr,lf   16              SET APPLICATION-MODE   12
                                     SET BAUD   12
          Del key   16               SET CLEAR-SCREEN   12
          Delay   9, 14, 17          SET Command   11
          DELETE Command   8         SET CURSOR-KEYS-VT100   12
          Dos   2                    SET DEBUGGING   12
          Dos filenames   2          SET DEFAULT-DISK   12
                                     SET DISPLAY   12
          Eight-bit-quote   16       SET ESCAPE   13
          End-of-line   16           SET FILE-TYPE   13
          Escape character   9       SET FILE-WARNING   13
          EXIT Command   8           SET FLOW   14
                                     SET KEYBOARD   14
          Game button   17, 18       SET LOCAL-ECHO   14
          GET Command   8            SET PARITY   14
                                     SET PREFIX   15
          HELP Command   9           SET PRINTER   15
                                     SET PROTOCOL   15
          Install   22               SET RECEIVE   15
          Integer   13               SET SEND   16
                                     SET SLOT   16
          Kermit   15                SET SWAP   16
          Kermit.help   22           SET TERMINAL   17
          Kermit.init   22           SET TIMER   16
          KERMIT.MODEM   9           SET TIMING   17
                                     SHOW command   18
          LOCK Command   9           Smart modem   9
          LOG Command   9            Start-of-packet   16
          LS Command   6             STATUS Command   21

          MODEM Command   9          TAKE Command   21
          Monitor   17               Text   13
                                     Timeout   16
          OA key   17, 18            TYPE Command   21
          Other   13
                                     UNLOCK Command   21
          Packet-length   16
          Pad-char   16              Vt100   17

Apple II Kermit                                                         Page 37

-------------------------------------------------------------------------------
          VT100 Emulation   17
          Vt52   17
          VT52 Emulation   17

          Xmodem   10, 15

Apple II Kermit                                                          Page i

-------------------------------------------------------------------------------
                               Table of Contents

1. Apple II Kermit                                                            1

   1.1. Supported Systems and Devices                                         2
   1.2. The DOS 3.3 File System                                               2
   1.3. The PRODOS File System                                                4
   1.4. Program Operation                                                     4
   1.5. Kermit-65 Commands                                                    6
       1.5.1. The CATALOG Command                                             6
       1.5.2. The CONNECT Command                                             6
       1.5.3. The DELETE Command                                              8
       1.5.4. The EXIT and QUIT Commands                                      8
       1.5.5. The GET Command                                                 8
       1.5.6. The HELP Command                                                9
       1.5.7. The LOCK Command                                                9
       1.5.8. The LOG Command                                                 9
       1.5.9. The MODEM Command                                               9
       1.5.10. The RECEIVE Command                                           10
       1.5.11. The REMOTE Command                                            10
       1.5.12. The RENAME Command                                            10
       1.5.13. The SEND Command                                              10
       1.5.14. The SERVER Command                                            11
       1.5.15. The SET Command                                               11
       1.5.16. the SHOW command                                              18
       1.5.17. The STATUS Command                                            21
       1.5.18. The TAKE Command                                              21
       1.5.19. The TYPE Command                                              21
       1.5.20. The UNLOCK Command                                            21
   1.6. Installation                                                         21
       1.6.1. Standard Installation                                          22
       1.6.2. Alternate Installation                                         23
   1.7. Problems                                                             24
   1.8. Customizing Kermit-65                                                31

Index                                                                        36

Apple II Kermit                                                         Page ii

-------------------------------------------------------------------------------
                                List of Figures

   Figure 1-1:   VT100 Keypad on an Apple Keyboard                           18
   Figure 1-2:   VT100 Keypad on an Apple//gs                                19
   Figure 1-3:   VT52 Keypad on an Apple Keyboard                            20

Apple II Kermit                                                        Page iii

-------------------------------------------------------------------------------
                                List of Tables

   Table 1-1:   Apple II Communication Cards Supported by Kermit-65           2
   Table 1-2:   Kermit-65 Single-Character CONNECT Escape Commands            7
   Table 1-3:   Apple II/II+ Keyboard Escapes                                 8
   Table 1-4:   Communications card vector area                              33
   Table 1-5:   PRODOS file types, part 1                                    34
   Table 1-6:   PRODOS file types, part 2                                    35