UUENCODE read a whole disk, uuencodes it and sends it
out on the serial line (slot 2 assumed). You can simply
capture it on the other side and pipe it thru uudecode.

UUENCODE.BAS is the main part (in Applesoft BASIC).
UUENCODE.ASS is the uuencoder in assembly language.

RWTS2 is needed also.
RWTS2 is a assembly language routine, which hooks into
the Applesoft &-vector. It allows simple access to the
DOS 3.3 RWTS (read write track sector) routine.

The following commands are understood:
	&A (ADDRESS,DRIVE)	set the buffer address and the drive
	&R (TRACK,SECTOR)	read the given sector into the buffer
	&W (TRACK,SECTOR)	write the buffer to the sector

ADDRESS is a pointer to a 256 byte buffer
DRIVE is 0 or 1
TRACK is 0 to 35
SECTOR is 0 to 15

If you want to access a disk drive in another slot (default=6),
you have to POKE 879,16*SLOT before &R (or &W) and
POKE 927,16*SLOT after the &R (or &W).

Example: Read the VTOC (Track 17, Sector 0) into the memory.

100 HIMEM: 16384 : REM Set himem to $2000
110 PRINT CHR$($);"BRUN RWTS2"
120 &A(16384,0) : REM Use $2000-$20FF as buffer
130 &R(17,0): REM Read VTOC

-------------------8<----------------8<----------------------
100  REM  UUENCODE DISK
110  HIMEM: 16384
120 AD = 16384:A0 = AD + 256
130  IF  PEEK (1013) = 76 AND  PEEK (1014) = 32 AND  PEEK (1015) = 3 THEN 160
140  PRINT  CHR$ (4)"BRUN RWTS2"
150  PRINT  CHR$ (4)"BRUN UUENCODE.BIN"
160  & A(A0,1)
170 A1 = A0
180  PR# 2
190  PRINT "BEGIN 666 DISK"
200  FOR T = 0 TO 34
210  FOR S = 0 TO 15
300  & R(T,S)
310 A2 = A0 + 256
400  IF A2 - A1 < 45 THEN 500
410  POKE 237,45
420  POKE 239,A1 / 256
430  POKE 238,A1 - 256 *  PEEK (239)
440  CALL 784
450 A1 = A1 + 45
460  GOTO 400
500  POKE 237,A2 - A1
510  POKE 239,A1 / 256
520  POKE 238,A1 - 256 *  PEEK (239)
530  CALL 787
540 A1 = A1 - 256
600  NEXT S
610  NEXT T
700  POKE 237,A2 - A1 - 256
710  POKE 239,A1 / 256
720  POKE 238,A1 - 256 *  PEEK (239)
730  CALL 784
800  PRINT " "
900  PRINT "END"
910  PR# 0
-------------------8<----------------8<----------------------
0270-   A9 4C       LDA   #$4C
0272-   8D 13 03    STA   $0313
0275-   8D 10 03    STA   $0310
0278-   A9 02       LDA   #$02
027A-   8D 15 03    STA   $0315
027D-   A9 8D       LDA   #$8D
027F-   8D 14 03    STA   $0314
0282-   A9 02       LDA   #$02
0284-   8D 12 03    STA   $0312
0287-   A9 A1       LDA   #$A1
0289-   8D 11 03    STA   $0311
028C-   60          RTS   
028D-   A4 ED       LDY   $ED
028F-   A5 EE       LDA   $EE
0291-   85 EC       STA   $EC
0293-   A5 EF       LDA   $EF
0295-   85 ED       STA   $ED
0297-   C6 ED       DEC   $ED
0299-   B1 EE       LDA   ($EE),Y
029B-   91 EC       STA   ($EC),Y
029D-   88          DEY   
029E-   10 F9       BPL   $0299
02A0-   60          RTS   
02A1-   A5 ED       LDA   $ED
02A3-   20 E7 02    JSR   $02E7
02A6-   A0 00       LDY   #$00
02A8-   C4 ED       CPY   $ED
02AA-   10 36       BPL   $02E2
02AC-   A9 00       LDA   #$00
02AE-   85 EC       STA   $EC
02B0-   B1 EE       LDA   ($EE),Y
02B2-   4A          LSR   
02B3-   66 EC       ROR   $EC
02B5-   4A          LSR   
02B6-   66 EC       ROR   $EC
02B8-   20 E7 02    JSR   $02E7
02BB-   C8          INY   
02BC-   B1 EE       LDA   ($EE),Y
02BE-   4A          LSR   
02BF-   4A          LSR   
02C0-   05 EC       ORA   $EC
02C2-   4A          LSR   
02C3-   4A          LSR   
02C4-   20 E7 02    JSR   $02E7
02C7-   B1 EE       LDA   ($EE),Y
02C9-   85 EC       STA   $EC
02CB-   C8          INY   
02CC-   B1 EE       LDA   ($EE),Y
02CE-   0A          ASL   
02CF-   26 EC       ROL   $EC
02D1-   0A          ASL   
02D2-   26 EC       ROL   $EC
02D4-   A5 EC       LDA   $EC
02D6-   20 E7 02    JSR   $02E7
02D9-   B1 EE       LDA   ($EE),Y
02DB-   20 E7 02    JSR   $02E7
02DE-   C8          INY   
02DF-   4C A8 02    JMP   $02A8
02E2-   A9 8D       LDA   #$8D
02E4-   4C ED FD    JMP   $FDED
02E7-   29 3F       AND   #$3F
02E9-   D0 02       BNE   $02ED
02EB-   A9 40       LDA   #$40
02ED-   18          CLC   
02EE-   69 A0       ADC   #$A0
02F0-   4C ED FD    JMP   $FDED
02F3-   00          BRK   
02F4-   00          BRK   
02F5-   00          BRK   
02F6-   00          BRK   
02F7-   00          BRK   
02F8-   00          BRK   
02F9-   00          BRK   
02FA-   00          BRK   
02FB-   00          BRK   
02FC-   00          BRK   
02FD-   00          BRK   
02FE-   00          BRK   
02FF-   00          BRK   

0270: A9 4C 8D 13 03 8D 10 03
0278: A9 02 8D 15 03 A9 8D 8D
0280: 14 03 A9 02 8D 12 03 A9
0288: A1 8D 11 03 60 A4 ED A5
0290: EE 85 EC A5 EF 85 ED C6
0298: ED B1 EE 91 EC 88 10 F9
02A0: 60 A5 ED 20 E7 02 A0 00
02A8: C4 ED 10 36 A9 00 85 EC
02B0: B1 EE 4A 66 EC 4A 66 EC
02B8: 20 E7 02 C8 B1 EE 4A 4A
02C0: 05 EC 4A 4A 20 E7 02 B1
02C8: EE 85 EC C8 B1 EE 0A 26
02D0: EC 0A 26 EC A5 EC 20 E7
02D8: 02 B1 EE 20 E7 02 C8 4C
02E0: A8 02 A9 8D 4C ED FD 29
02E8: 3F D0 02 A9 40 18 69 A0
02F0: 4C ED FD 00 00 00 00 00
02F8: 00 00 00 00 00 00 00 00
-------------------8<----------------8<----------------------

0300-   A9 4C       LDA   #$4C
0302-   8D F5 03    STA   $03F5
0305-   A9 20       LDA   #$20
0307-   8D F6 03    STA   $03F6
030A-   A9 03       LDA   #$03
030C-   8D F7 03    STA   $03F7
030F-   60          RTS   
0310-   04          ???   
0311-   C6 51       DEC   $51
0313-   F0 08       BEQ   $031D
0315-   CA          DEX   
0316-   D0 F6       BNE   $030E
0318-   A6 50       LDX   $50
031A-   4C 0B 03    JMP   $030B
031D-   60          RTS   
031E-   00          BRK   
031F-   4A          LSR   
0320-   C9 52       CMP   #$52
0322-   F0 0F       BEQ   $0333
0324-   C9 57       CMP   #$57
0326-   F0 0F       BEQ   $0337
0328-   EA          NOP   
0329-   EA          NOP   
032A-   EA          NOP   
032B-   EA          NOP   
032C-   C9 41       CMP   #$41
032E-   F0 1D       BEQ   $034D
0330-   4C 7C D9    JMP   $D97C
0333-   A9 01       LDA   #$01
0335-   D0 02       BNE   $0339
0337-   A9 02       LDA   #$02
0339-   85 FA       STA   $FA
033B-   20 B5 03    JSR   $03B5
033E-   20 46 E7    JSR   $E746
0341-   86 FC       STX   $FC
0343-   A5 50       LDA   $50
0345-   85 FB       STA   $FB
0347-   20 B8 DE    JSR   $DEB8
034A-   4C 65 03    JMP   $0365
034D-   20 B5 03    JSR   $03B5
0350-   20 46 E7    JSR   $E746
0353-   8A          TXA   
0354-   EA          NOP   
0355-   EA          NOP   
0356-   EA          NOP   
0357-   EA          NOP   
0358-   85 FF       STA   $FF
035A-   A5 50       LDA   $50
035C-   85 FD       STA   $FD
035E-   A5 51       LDA   $51
0360-   85 FE       STA   $FE
0362-   4C B8 DE    JMP   $DEB8
0365-   20 E3 03    JSR   $03E3
0368-   84 06       STY   $06
036A-   85 07       STA   $07
036C-   A0 01       LDY   #$01
036E-   A9 60       LDA   #$60
0370-   91 06       STA   ($06),Y
0372-   C8          INY   
0373-   A5 FF       LDA   $FF
0375-   91 06       STA   ($06),Y
0377-   C8          INY   
0378-   A9 00       LDA   #$00
037A-   91 06       STA   ($06),Y
037C-   C8          INY   
037D-   A5 FB       LDA   $FB
037F-   91 06       STA   ($06),Y
0381-   C8          INY   
0382-   A5 FC       LDA   $FC
0384-   91 06       STA   ($06),Y
0386-   A0 08       LDY   #$08
0388-   A5 FD       LDA   $FD
038A-   91 06       STA   ($06),Y
038C-   C8          INY   
038D-   A5 FE       LDA   $FE
038F-   91 06       STA   ($06),Y
0391-   A0 0C       LDY   #$0C
0393-   A5 FA       LDA   $FA
0395-   91 06       STA   ($06),Y
0397-   A0 0E       LDY   #$0E
0399-   A9 00       LDA   #$00
039B-   91 06       STA   ($06),Y
039D-   C8          INY   
039E-   A9 60       LDA   #$60
03A0-   91 06       STA   ($06),Y
03A2-   A4 06       LDY   $06
03A4-   A5 07       LDA   $07
03A6-   20 D9 03    JSR   $03D9
03A9-   A9 00       LDA   #$00
03AB-   85 48       STA   $48
03AD-   A0 0D       LDY   #$0D
03AF-   B1 06       LDA   ($06),Y
03B1-   85 1D       STA   $1D
03B3-   60          RTS   
03B4-   00          BRK   
03B5-   20 B1 00    JSR   $00B1
03B8-   4C BB DE    JMP   $DEBB
03BB-   29 2A       AND   #$2A
03BD-   2B          ???   
03BE-   00          BRK   

0300: A9 4C 8D F5 03 A9 20 8D
0308: F6 03 A9 03 8D F7 03 60
0310: 04 C6 51 F0 08 CA D0 F6
0318: A6 50 4C 0B 03 60 00 4A
0320: C9 52 F0 0F C9 57 F0 0F
0328: EA EA EA EA C9 41 F0 1D
0330: 4C 7C D9 A9 01 D0 02 A9
0338: 02 85 FA 20 B5 03 20 46
0340: E7 86 FC A5 50 85 FB 20
0348: B8 DE 4C 65 03 20 B5 03
0350: 20 46 E7 8A EA EA EA EA
0358: 85 FF A5 50 85 FD A5 51
0360: 85 FE 4C B8 DE 20 E3 03
0368: 84 06 85 07 A0 01 A9 60
0370: 91 06 C8 A5 FF 91 06 C8
0378: A9 00 91 06 C8 A5 FB 91
0380: 06 C8 A5 FC 91 06 A0 08
0388: A5 FD 91 06 C8 A5 FE 91
0390: 06 A0 0C A5 FA 91 06 A0
0398: 0E A9 00 91 06 C8 A9 60
03A0: 91 06 A4 06 A5 07 20 D9
03A8: 03 A9 00 85 48 A0 0D B1
03B0: 06 85 1D 60 00 20 B1 00
03B8: 4C BB DE 29 2A 2B 00 2C